## Slide 1: Single Particle Motion
Alexis Briesemeister
Oak Ridge National Lab
Presented:
June 8th 2015
SULI Introductory Course in Plasma Physics
Notes: Post-Doc at Oak Ridge National Lab, but I currently live in San Diego and work on the DIII-D tokamak

## Slide 2: Motivation: Single particle motion and collisions limit plasma confinement
Plasma transport can be described as a “random walk”
  single particle motion gives the step size
  collision frequency tells you how often steps are taken
If care isn’t taken to optimize your magnetic field geometry particles can have trajectories which cause them to leave the system even without collisions
  High energy particles are the most susceptible and the most damaging

## Slide 3: The 3 things you should walk away from this talk with:
Charged particles move freely along a constant magnetic field, but any velocity perpendicular to the field causes them to orbit around the field lines
When the magnetic field strength isn’t constant it will change parallel velocity of the charged particle and cause it to drift off the field line
A force perpendicular to your field lines will cause the particle to move perpendicular to both the force and the magnetic field lines

## Slide 4: Resources Available Online
NRL Plasma Formulary
  www.nrl.navy.mil/ppd/content/nrl-plasma-formulary
Magnetic Fusion Energy Formulary
  www.psfc.mit.edu/research/MFEFormulary/
Fusionwiki
  fusionwiki.ciemat.es/
Introduction to Plasma Physics and Controlled Fusion by F. Chen
Notes: Knowing where to find things can be more important than knowing thngs.

## Slide 5: Section 1: Neutral particles

## Slide 6: Section 1: Neutral particles
Ballistic.

## Slide 7: Section 1: Neutral particles travel ballistically
Not confined by magnetic fields
  Neutrons generated by the D+T fusion process travel directly to the wall
Neutral particles are very relevant near material interfaces
  But their single particle motion is not very interesting

## Slide 8: Section 2:(AKA The rest of this talk) CHARGED particles
Electrons
Ions
Very highly charged, extremely small dust particles

## Slide 9: Lorentz force equation forms the basis for single particle motion
Lorentz force describes the forces on a charged particle moving in a the presence of an electric field and magnetic field
  =force on the particle
  =charge on the particle
  = electric field
  =velocity of the particle
  =magnetic field

## Slide 10: Newton’s law second law of motion also important
Newton’s second law of motion
  =force on the particle
  =mass of that particle
  = acceleration of that particle

## Slide 11: Charged particles move freely ALONG magnetic fields
Particles are free to stream along magnetic field lines
  …when the magnetic field is constant
0
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 12: Cyclotron-frequency and Larmor radius
Cyclotron-frequency (aka gyro-frequency) the frequency at which a particle moves around the magnetic field:
Larmor radius the radius of the orbit the particle:

## Slide 13: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 14: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 15: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 16: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 17: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 18: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg
Charged particles move freely along the magnetic field!

## Slide 19: Charged particles in a magnetic field
z
y
x
Figure from: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg

## Slide 20: Motion perpendicular to the magnetic field

## Slide 21: Drop the unit vectors

## Slide 22: Take another derivative with respect to time

## Slide 23: The goal: differential equations which involve a single spatial coordinate

## Slide 24: Repeat for the terms involving x

## Slide 25: 2 equations each with involving a single spatial coordinate

## Slide 26: 2 differential equations can be solved using sines and cosines
could be an arbitrary coefficient, but is constrained by the initial velocity perpendicular to
An arbitrary phase is used to match the initial velocity

## Slide 27: Integrate to find the position
2 equations to describe the particle’s position in the plane perpendicular to the magnetic field

## Slide 28: Particles make circular orbits, with a handedness that depends on charge
y
x
z
rL

## Slide 29: Larmor radius set the MINIMUM size for a confinement device
y
x
z
rL
Picture: LAPD linear plasma device
Devices must be much larger than the Larmor radii of the particles they are confining

## Slide 30: Ions are a lot heavier than electrons
protons are about 1800 times heavier than electrons

## Slide 31: Ions generally have much larger Larmor radii than electrons
Energy tends to equilibrate in the system

## Slide 32: Cyclotron frequency
Important for particle heating
Electron cyclotron frequency in a 1 Tesla magnetic fields is 28.0 GHz
Ion cyclotron frequency in a 1 Tesla magnetic fields is 14.2 MHz
Your microwave oven operates at 2.45 GHz
The FM radio band is from 88 to 108 MHz

## Slide 33: Electric field parallel to magnetic field
If the electric field is parallel to the magnetic field the charge particles are accelerated just like they would be if there was no magnetic field

## Slide 34: Electric field PERPENDICULAR to the magnetic field
Diagram from: http://www.newworldencyclopedia.org/entry/File:Charged-particle-drifts.svg#file
B
Particles are accelerated when traveling along the electric field direction and decelerated when traveling against it
This alters the gyromotion causing the particles to drift

## Slide 35: Other forces cause drifts which push positive and negative particles in opposite directions
One example of this is drift caused by the gravitational force:
Is given by:
…but will generally be much weaker than the other forces in your system

## Slide 36: Particle motion in a non-uniform magnetic field
In gyro-radius will be larger where the field is weaker and smaller where the field is stronger
The resulting velocity is described by:

## Slide 37: Total particle motion in a curved magnetic field
The resulting velocity is described by:

## Slide 38: 3 invariant quantities
These quantities don’t change unless something does work on the particle
Magnetic fields do not do work on the particles
Magnetic moment:
Energy:
Adiabatic invariant:

## Slide 39: The magnetic moment of a gyrating particle is a conserved quantity
As a particle moves to a region of larger magnetic field, the particles velocity perpendicular to the field must also increase
Magnetic moment

## Slide 40: The conservation of the magnetic moment and conservation of energy creates the mirror effect
As the particle’s increase to conserve the particle’s must decrease to conserve energy
The particle’s initial energy
The particle’s energy at any given time

## Slide 41: Adiabatic invariant
The integral of the parallel velocity as a particle bounces between two points stays constant

## Slide 42: Magnetic mirrors were one of the first plasma confinement devices
Picture from http://en.wikipedia.org/wiki/Magnetic_mirror#/media/File:Basic_Magnetic_Mirror.jpg
The magnetic field prevents the particles from traveling radially towards the wall
Particles are reflected by in the regions of higher magnetic field

## Slide 43: Non-uniform magnetic fields in mirror machines can be used to confine particles
Q-cumber 1955
http://en.wikipedia.org/wiki/Tandem_Mirror_Experiment
https://www.flickr.com/photos/llnl/page4
Tandem mirror 1979
Both machines were at Lawrence Livermore National Lab

## Slide 44: Lockhead Martin’s “compact fusion reactor”
Pictures from:
http://aviationweek.com/technology/skunk-works-reveals-compact-fusion-reactor-details
Figures released show a confinement scheme similar to previous magnetic mirror confinement devices

## Slide 45: Some particles will always escape
Any particles with sufficient parallel velocity will escape
Loss cone can be narrowed by increasing the magnetic field at the throat of the device
Collisions constantly replenish the loss cone
Picture from: http://en.wikipedia.org/wiki/Magnetic_mirror#/media/File:Basic_Magnetic_Mirror.jpg
Lost
Confined
Confined
Lost

## Slide 46: A circular magnetic field doesn’t have end loss problems…but it does have other problems
Picture from: https://www.thunderbolts.info
Electrical Current
B
Plasma
Z-pinch: a current is driven in the plasma to create a the confining magnetic field
These configurations are unstable to kink modes
A kink instability

## Slide 47: Curved fields cause particles to drift off the field lines
Particles will drift in a direction normal to both the magnetic field and the radius of curvature
These drifts always add
B
RC
Drift direction

## Slide 48: Magnetic fields that wrap both the short and long way around a toroidal device compensate for drifts off a surface
Tokamaks have both and externally generated toroidal field
And a poloidal field generated by driving a current through the plasma
Picture from: http://www.alternative-energy-action-now.com/tokamak-fusion-reactor.html
Poloidal B
Toroidal B
Total B
Toroidal Current
Toroidal
Coils

## Slide 49: Poinecaré Plot
A slice of the tokamak at a given toroidal angle
RC

## Slide 50: Passing particle
Particles with sufficient velocity will leave their original flux surface but will make a full poloidal transit
RC
VD
+

## Slide 51: Trapped particles
Particles with lower parallel velocity will become trapped in “banana” orbits
This increases plasma diffusion
RC
VD
+ the mirror force
+

## Slide 52: Banana orbits move around the torus
dfd
Picture from: https://www.euro-fusion.org/wpcms/wp-content/uploads/2011/09/jg05-537-4c.jpg

## Slide 53: Stellarator: both poloidal and toroidal field are generated using external coils
Complicated coil structure leads to more complicated field structure and more complicated particle orbits
Picture W7-X: physics.ucla.edu/icnsp/Html/spong/spong.htm

## Slide 54: Stellarator have super bananas
Trapped particles can precess poloidally around stellarators
If stellarator fields are not optimized these particles will end up trajectories which intersect the wall
Picture from: http://web.ornl.gov/sci/fed/mhd/QOS_Orbits.html
Passing
Trapped
Deeply Trapped

## Slide 55: Conclusion
Although particles are free to move along magnetic field lines, drifts push particles way from their original field lines
Toroidal confinement devices have magnetic fields in both the poloidal and toroidal direction to compensate for these drifts
Regions of strong magnetic fields can reflect particles with with insufficient velocity to overcome the mirror effect