## Slide 1: Stellarator Physics and Design
D. A. Gates
SULI Seminar
June 29, 2017

## Slide 2: Toroidal Magnetic Confinement
flux surface y
Bq
BF
Poloidal
direction
i
Requires a poloidal (Θ) component of B so that cross-field particle drifts average to zero over the particle orbit
For example, in a tokamak, BxB drift is vertical; discharge would drift out of confinement region without Bq
B
BxB
Two methods to produce magnetic transform
i = 1/q ~ Bq /Bf
Plasma current
  Tokamaks, reversed field pinches, spheromaks
  All toroidally symmetric
Non-symmetric helically deformed fields
      Stellarators

## Slide 3: Stellarator history
Concept invented by Lyman Spitzer et al (1958)
  Phys. Fluids 1 (1958) 253.
Helical fields
  B = BT + BP
  Both field components generated by coils
Linear Stellarators
  Helically symmetric system: f = θ – az
    2 alternating currents
    Not required to be same amplitude
Produces flux surfaces
Which rotate helically
l=1
l=2
l=3

## Slide 4: Historically, stellarators had poor confinement when compared to tokamaks

## Slide 5: Stellarator history (continued)
To confine plasma axially and eliminate endlosses, bend a linear stellarator into a torus
  This breaks the helical symmetry
  Resultant system will not be toroidally symmetric
Stellarator designs from 1958 through ~1988 attempted to produce configurations that required coils or fields that “looked” symmetric (in one sense or another)
Since ~1988, stellarators have been numerically designed to have the desired plasma characteristics
  E.g. symmetric-like orbits (even though they don’t “look” symmetric)
Stellarators with numerically designed coilsets to produce “symmetric” fields:
  HSX – operating since 1999
  Wendelstein7-X operated this year (quasi-omnigeneous)
  NCSX (mostly constructed, but project cancelled)

## Slide 6: Asymmetric variation in |B| cause for radial drift

## Slide 7: Three different types of optimization
Quasi-Axisymmetry
(QUASAR)
Quasi-Isodynamic
(W7-X)
Quasi-helicalsymmetry
(HSX)

## Slide 8: Neoclassical losses in classical stellarators

## Slide 9: Trajectories in an optimized stellarator

## Slide 10: Neoclassically Optimized Configurations
Three types of neoclassical optimization
US has substantial expertise in quasi-symmetry
Quasi-axisymmetry (QA)
NCSX
Bootstrap current increases
transform
Bootstrap current is large
Can be designed at lower
aspect ratio
Quasi-omnigeneity (QO)
W7-X
Bootstrap current can be
made to cancel ~0
High aspect ratio
Quasi-helical symmetry (QH)
HSX
Bootstrap current reduces
transform
Bootstrap current is lower
than QA
High aspect ratio

## Slide 11: Stellarator issues
Lack of “natural” symmetry in toroidal stellarators
  Stellarators do not automatically have closed flux surfaces
  Stellarators do not automatically have closed drift surfaces
  Therefore, stellarators must be carefully designed to confine particle orbits
Lack of physical symmetry ➪ lack of symmetry in coil geometry
  Coils are complex
  Complex coil shape must be produced with ~few millimeter accuracy
Field geometry can be beta dependent - pressure driven currents can modify equilibrium
  Solutions:
    Suppress pressure-driven currents (mirror terms, Wendelstein-family solution)
    Optimize design around pressure driven currents (NCSX approach)
No significant Ohmic heating
  Inherently not steady-state, but very inexpensive for tokamaks

## Slide 12: Stellarators provide attractive path to electricity production
Energy mission requires efficiency
  Stellarators minimize recirculating power!
The advantages of the stellarator
  Device size and confinement requirements are modest
  Operating space much wider (higher density limit)
Modern stellarator confinement database sufficient for reactor
New design tools being employed to design a mission relevant device

## Slide 13: Key metric is overall electrical efficiency: Qeng
th = thermal conversion efficiency
aux = injected power wall plug efficiency
Q = fusion power / auxiliary power
Mn = neutron energy multiplier
Pn = neutron power from fusion
P = alpha power from fusion
Paux = injected power (heat + CD + control)
Ppump = coolant pumping power
Psub = subsystems power
Pcoils = power lost in coils (Cu)
Pcontrol = power used in plasma or plant control that is not included in Pinj
Pextra = Ppump + Psub + Pcoils + Pcontrol
Blanket and auxiliary power efficiency + fusion gain largely determine electrical efficiency Qeng
Electricity produced
Electricity consumed

## Slide 14: It’s easier to make electricity in a stellarator
Fixed Magnetic field at the Coil (14T)
“Pilot Plants”, J. Menard, Nucl. Fusion 51 (2011) 103014
But makes net electricity
Stellarator has the lowest fusion power…
Similar sizes

## Slide 15: Movie Time
The end of a stellarator shot
The end of a tokamak shot

## Slide 16: W7-X will operate near the assumed confinement times for CS pilot plant
ISS04 database contains many points that cover the assumed pilot plant multiplier values
The stellarator database only goes up to tE ~ 200ms
  tokamaks are up to tE ~ 1s
  W7-X achieve values in this range
  Stellarator extrapolation is larger
ISS95 scaling law with tokamak and stellarator data
CS Pilot Plant

## Slide 17
W7-X Major device components
plasma
five roughly identical modules
50 non-planar 20 planar SC coils
He pipes
254 ports
access domes and instrumentation plugins
cryostat vessel ~ 500 openings
3d-shaped plasma vessel
2500 in-vessel components
14 HTSC current leads
SC bus bar
cryo feet
machine base
central support ring
thermal insulation MLI and He gas cooled shield

## Slide 18
W7-X Facts and figures
T. Klinger on Wendelstein 7-X 18
five magnetic field periods
modular non-planar coils
quasi-isodynamic equilibrium
low bootstrap current O(10 kA)
high iota and low shear
flexible magnetic field configurations
735 t mass with 435 t cold mass
70 superconducting NbTi coils
3 T magnetic induction on axis
254 ports of 120 different types
30 m3 plasma volume
265 m2 in-vessel components
4.5m height and 16 m diameter

## Slide 19
Physics optimisation
T. Klinger on Wendelstein 7-X 19
high quality of vacuum magnetic surfaces
good finite equilibrium properties @ < > = 5%
good MHD stability properties @ < > = 5%
reduced neoclassical transport in 1/ -regime
small bootstrap current in lmfp-regime
good collisionless fast particle confinement
good modular coil feasibility
seven optimisation criteria
3d computer codes
vacuum field and coils
MHD equilibrium
MHD linear stability
neoclassical transport
Monte Carlo test particle
edge and divertor

## Slide 20
Machine base
T. Klinger on Wendelstein 7-X 20

## Slide 21
Superconducting magnets
T. Klinger on Wendelstein 7-X 21
coil in the assembly handling unit
coil in the test bed @ CEA Saclay

## Slide 22
Superconducting magnet module
T. Klinger on Wendelstein 7-X 22

## Slide 23
Magnet module with central ring
T. Klinger on Wendelstein 7-X 23

## Slide 24
Integation of magnets and cryostat
T. Klinger on Wendelstein 7-X 24

## Slide 25
The device is complete
T. Klinger on Wendelstein 7-X 25

## Slide 26: Movie Time
W7-X time lapse

## Slide 27: HSX: the Helically Symmetric Experiment
Major Radius | 1.2 m
Minor Radius | 0.12 m
Number of Field Periods | 4
Coils per Field Period | 12
Rotational Transform | 1.05 1.12
Magnetic Field | 0.5 T
ECH Power (2nd Harmonic) | <100 kW 28 GHz

## Slide 28
Cutaway view of accessible stellarator – straight out legs
Simplified Coils
Using Improved Algorithms
Coils now represented as splines rather than as Fourier series
  Has been used to design a device with clear access for maintenance
Technique facilitates any set of spatial constraints
Coils and winding surface

## Slide 29: Stellarators can solve many of the problems of fusion energy
Good confinement
Steady state operation
High density and temperature
W7-X is leading the way in optimized stellarator operation

## Slide 30: Symmetry can be Broken with Auxiliary Coils
Aux coils add n=4 and 8, m=0 terms to the magnetic spectrum
  Called the Mirror configuration
  Raises neoclassical transport towards that of a conventional stellarator
Other magnetic properties change very little compared to QHS
  Separates the effects of the magnetic spectrum on transport
Mirror Magnetic Spectrum
Rotational Transform
Well Depth

## Slide 31: Core Mirror Symmetry Breaking is Large
εeff at r/a = 2/3
QHS: 0.005
Mirror: 0.04
C.D. Beidler et al., PPCF 36 (1994) 317

## Slide 32: Neoclassical Transport is Reduced in the Quasisymmetric Configuration
Monoenergetic diffusion coefficients calculated with Drift Kinetic Equation Solver (DKES*)
Data is fit to an analytic form, including 1/ν, ν1/2, and ν regimes of low-collisionality transport
Integration over Maxwellian forms thermal transport matrix
*W.I. van Rij and S.P. Hirshman, Phys. Fluids B 1, 563 (1989).
Mirror
QHS
Er
HSX Parameters

## Slide 33: The Ambipolar Electric Field has a Large Effect on Neoclassical Transport
Electric field is determined by ambipolarity constraint on neoclassical fluxes
This has up to three solutions: the ion and electron roots, and an unstable intermediate root
In HSX plasmas Te >> Ti
  In Mirror, only electron root exists
  Large electric field reduces Mirror transport/neoclassical differences with quasisymmetric field
HSX Parameters:
Te >> Ti
Te ~ Ti

## Slide 34: Large Differences are Observed between QHS and Mirror Profiles
Plasma density and temperature profiles are measured with a 10-channel Thomson scattering system
Discharges shown: ~50 kW of ECRH power, central deposition
QHS has higher temperature, more peaked density profile
Electron Temperature
Electron Density

## Slide 35
Stellarator Divertor Approaches
LHD
W 7X
NCSX
3 Different strategies for stellarator divertors: islands vs stochastic spreading
Need to test experimentally: exhaust handling, impurity control
Controlled detachment obtained in LHD and W7X.

## Slide 36
Smoother Coils at Higher Aspect Ratio
A = 6
A = 4
A = 8
Aspect ratio scan, all have iota-vac=0.3, kink/RWM stable
Shown with constant volume. Larger A  larger R
Increasing aspect ratio reduces coil distortion, disentangles coils
All these coil designs can likely be built. Which is best?
What aspect of simplicity is important?