## Slide 1
PLASMA EXHAUST VIA A MAGNETIC DIVERTOR
Rajesh Maingi
Princeton Plasma Physics Laboratory
SULI summer lecture
July 11, 2019
Princeton, NJ

## Slide 2: Outline
Introduction to magnetic confinement and tokamaks
Plasma exhaust via magnetic X-point divertors
  Particle exhaust
  Momentum and power exhaust
  Recently identified challenges to attractive core-edge plasma scenarios with W walls
Types of transient events, and their impact
2

## Slide 3: Critical challenge for fusion: keeping the core hot and and the plasma facing components ‘cold’
Solid material limits
Need to exhaust
Plasma particles
Plasma momentum
Plasma energy
3
1 eV ~ 11,600 K

## Slide 4: Ways of confining plasmas
Requires large
amounts of mass!
Confines the plasma in the direction across the magnetic field
Energy and defense
relevant
4

## Slide 5: Origin of the tokamak
Original idea was to use a concentrated magnetic field on the end of a linear system, to reflect particles back into main chamber (‘magnetic mirror’)
  Suffered from ‘end loss cone’
In the 1960’s, Russian scientists proposed a doughnut-shaped device with ‘axial’ or toroidal magnetic field for stability, and ‘azimuthal’ or poloidal field for confinement, driven by a current in the plasma
  Particles saw no beginning or end -> high confinement!
Toroidal field coils
Plasma current
5

## Slide 6: ‘H-mode’: a strong gradient of density, temperature & pressure near plasma edge
6
NSTX-U data,
Courtesy of D. Battaglia
Sharp increase in edge density, temperature, pressure observed in tokamaks in 1982 – called ‘H-mode’
Core sits on top of a ‘pedestal’ – more stored energy for same input power –> improved energy confinement

## Slide 7: ‘H-mode’: a strong reduction in edge plasma turbulence
7
NSTX data, Courtesy of S. Zweben

## Slide 8: The international fusion community has agreed to build a large tokamak toward energy production
ITER
Seven international partners
  EU
  Japan
  US
  Russia
  China
  Korea
  India
Being built in France
  First plasma ~ Dec. 2025
Pfusion = 500 MW for 1000 sec discharges
Pfusion = 250 MW in steady state
8

## Slide 9: Plasma-material interactions: how do you keep the hot part hot and the cold part cold?
Answer: mass difference!
  In ITER, there is less than ½ gram of deuterium and tritium in the core
  The total mass of ITER is nearly 50 million pounds; a fraction of this is in the plasma facing components, which will absorb the heat
  The internal components of ITER will be actively cooled to keep temperature below melt limits
    The key is to maximize heat dispersal area
The present technological heat flux removal limit for solids is about 10 MW/m2
  A rocket nozzle has average heat flux of 1 MW/m2!
  The sun’s radiant heat flux on earth ~ 1400 W/m2
9

## Slide 10: Outline
Introduction to magnetic confinement and tokamaks
Plasma exhaust via magnetic X-point divertors
  Particle exhaust
  Momentum and power exhaust
  Recently identified challenges to attractive core-edge plasma scenarios with W walls
Types of transient events, and their impact
10
R. Maingi, ‘Plasma Exhaust’, chapter in Magnetic Fusion Energy: from Experiments to Power Plants, G.H. Neilson, editor, Woodhead Publishing, Elsevier Press, (2016) 31-59.

## Slide 11: Limiters and divertors used to exhaust plasma
11
A limiter is a surface in contact with the plasma
  Can be inserted (sacrificial) or part of surrounding wall structure
  Examples of inner wall and outer wall limiters shown at right
If external current is run in the same direction as plasma current outside of the confined plasma, then one component of the field can be canceled, creating an X-point divertor
Bq=I/(2πa)

## Slide 12: Divertors used to exhaust plasma and reduce PMI at wall
12
Y. Feng et. al., Nucl. Fusion 46 (2006) 807
edge
SOL
SOL = Scrape-Off
Layer
In a divertor, edge plasma flows across closed magnetic flux surfaces into the scrape-off layer
Plasma flows along open magnetic field lines in the SOL to the divertor target
  Can have one or more X-points, e.g. 1, 2, or even 8!

## Slide 13: Divertors, cryopumps, and structures to restrict neutral flow (baffles) can provide particle control
13
M. Wade et. al., PRL 74 (1995) 2702
M.A. Mahdavi et. al., J. Nucl. Mater. 220-222 (1995) 13
Both D/T (fuel) and He (ash) need to be exhausted
In-vessel cryopumps control deuterium and He inventory
  Divertor particle flux can be captured and exhausted
  ITER designed with cryos
R. Maingi et. al., Nucl. Fusion. 39 (1999) 1187

## Slide 14: Tritium retention is a central element of particle exhaust, and strongly affected by choice of PFC materials
14
G. Federici et. al., Nucl. Fusion 41 (2001) 1967
Graphite was PFC of choice in 90’s, but it captures hyrogenic species via unsaturable co-deposition
  e.g. Graphene & Zn shown on right
C advantages
  Good power handling, good thermal shock and thermal fatigue resistance (low crack propagation)
  Doesn’t melt (but sublimes), low radiated power
  Good joining technology, low-Z
C disadvantages
  Chemical erosion and co-deposition; dust generation
  May require conditioning
  Physical and mechanical properties degrade w/low neutron fluence
  Roubin et al., J. Nucl. Mater. 390-391 (2009) 49
Co-deposits in Tore Supra

## Slide 15: W chosen for divertor & Be for wall of ITER
15
G. Federici, et. al., Nucl. Fusion 41 (2001) 1967
W advantages
  Low physical sputtering yield; high threshold
  No chemical sputtering with hydrogen
  Low in-vessel tritium retention at T < 500 oC
  Reparable by plasma spray; good joining technology
W disadvantages
  Low allowable core concentration
  Melts under large transient loads
  High ductile-brittle transition temperature
  Recrystallizes (embrittles) at temperatures >1500 K
  High activation
  Blisters and generates ‘fuzz’ under He bombardment
  Confinement reduced in tokamaks as compared with carbon PFCs

## Slide 16: Components in present and past fusion devices
16
Device | Lim/Div | PFC mat’l | Device | Lim/Div | PFC mat’l
JET (2012+) | Divertor | W div. & Be wall | JET | Divertor | Carbon
ASDEX-U | Divertor | W divertor & wall | ASDEX-U | Divertor | Carbon
C-Mod | Divertor | Mo divertor & wall | DIII-D | Divertor | Carbon
NSTX | Divertor | C Wall/Li coating | NSTX-U plan | Divertor | High-Z + Liq. Li
RFX | Limiter | Liq. Li - Mo mesh | LTX | Limiter | Liq. Li on SS
JT-60U | Divertor | Carbon | TFTR | Limiter | Carbon
Tore Supra | Limiter | Carbon | West | Divertor | W wall
EAST | Divertor | W upper, Mo wall, C lower | KSTAR | Divertor | Carbon
MAST-U | Divertor | Carbon | COMPASS | Divertor | Carbon

## Slide 17: Critical challenge: keeping the core hot and and the plasma facing components ‘cold’ via magnetic divertors
Solid material limits
Need to exhaust
Plasma particles
  Recapture tritium
Plasma momentum
  Plasma is spinning in the core, either spontaneously or from momentum injection
  Sheath accelerates ions at PFCs
Plasma energy
  Plasma heated by fusion, simulated with neutral beams & RF heating
17
1 eV ~ 11,600 K
B.L. LaBombard et. al., Phys. Plasmas 2 (1995) 2242

## Slide 18: Plasma momentum exhaust
18
Plasma spins in the core spontaneously, which is good for stability and confinement
  Problem if rotation goes to zero (locked mode) – confinement loss
Sheath forms at PFC for equal ion and elec. flux
  Pre-sheath accelerates ions to sonic speed
    Bohm criterion: local Mach number u/cs = 1
  Sheath accelerates ions through a ~ 3kTe potential drop
  This plasma momentum is naturally exhausted at PFCs
Charge exchange between plasma ions and neutrals (recycling, beam input) reduces plasma momentum
  Becomes important for Te < 10 eV
  Manifests as a reduction in plasma pressure at low Te
Courtesy of J.L. Terry

## Slide 19: Power flow in the scrape-off layer to the divertor depends on density and collisionality
19
Sheath-limited: the midplane and divertor Te are about equal
  Pressure is same at midplane and divertor
Flux-limited: the divertor Te is below midplane
  Pressure is same at midplane and divertor
Detached: the divertor Te is ~ 1-2 eV
  Pressure in divertor well below midplane
  Recombination observed
B.L. LaBombard et. al., Phys. Plasmas 2 (1995) 2242
Sheath Flux Detached

## Slide 20: Divertor radiation and detachment used to reduce plasma heat flux onto PFCs
20
C.S. Pitcher et. al., Plasma Phys. Contr. Fusion 39 (1997) 779
At high density, divertor radiation occurs somewhere between the X-point divertor and PFC
  Low-Z impurity radiation zone: 1-10 eV
  Deuterium ionization front: 5 eV
  Recombination zone: 1-2 eV
Can be represented in 1-D
A.W. Leonard et. al., PRL 78 (1997) 4769
M.E. Fenstermacher et. al., Plasma Phys.
Contr. Fusion 41 (1999) A345

## Slide 21: Limit to detachment: intense radiation zone gets to X-point
21
When impurity radiation is present, certain Te ranges have a positive radiation-temperature feedback
  Lower Te -> more radiation!
  Condensation instability: MARFE
  MARFE = Multi-faceted Axisymmetric Radiation From the Edge, and earl MARmar & steve wolFE (MIT)
Limit to detachment: if MARFE migrates to X-point, tE reduced
Alcator C-Mod Dg emission data,
Courtesy of J.L. Terry

## Slide 22: Difficulties for W PFCs to achieve attractive, self-consistent core-edge scenarios have been identified
22
Power exhaust challenge harder than thought
  Heat flux footprint decreases with Ip; no increase with R
    Both steady and transient loads can exceed solid PFC limits
Confinement difficult with bare high-Z PFCs
  Good confinement is challenging with high-Z walls in e.g. JET
Outline
Plasma exhaust via magnetic X-point divertors
  Particle exhaust
  Momentum and power exhaust
  Recently identified challenges to attractive core-edge plasma scenarios with W walls

## Slide 23: Heat flux profile measured in divertor with infrared thermography & compared to midplane ne and Te profiles
23
lnmid
lqdiv,SOL
lqdiv,PFR
lTmid
M.A. Makowski et. al., Phys. Plasmas 19 (2012) 056122

## Slide 24: Steady heat flux flows in the SOL in a very narrow channel
24
Heat flux profile width lq measured in divertor
  lq projected to outer midplane with flux expansion
International effort found that lq varies inversely with Bpol,MP
  No increase with R, PSOL
  Low gas puff attached plasmas; some broadening and heat flux dissipation with detachment
Projected width in ITER ~ 1/5 previous value; peak heat flux 5x higher unless mitigated
Much more challenging for reactors, due to higher Pfusion
T. Eich et. al., Nucl. Fusion 53 (2013) 093031
ITER

## Slide 25: Edge and core plasma temperature and confinement was reduced in JET scenarios with installation of ITER-like wall
25
M. Beurskens et al., PPCF 55 (2013) 124013

## Slide 26: Several divertor innovations may increase the heat dispersal area for future (and present!) devices
26
Snowflake divertors
+ -
P. Valanju et. al., Nucl. Fusion 16 (2009) 056110
D. Ryutov et. al., Phys. Plasmas 14 (2007) 064502
Super-X divertor in MAST-Upgrade

## Slide 27: Liquid metal PFCs are an option to solid PFCs, but have substantial R&D needs to assess viability
27
Advantages
  Erosion tolerable from PFC view: self-healing surface
  No dust; main chamber material and tritium transported to divertor could be removed via flow outside of tokamak
  Liquid metal is neutron tolerant; protects substrate from PMI
  Liquid (and solid) lithium offer access to low recycling, high confinement regimes under proper conditions
  Very high steady, and transient heat exhaust, in principle (50 MW/m2 from electron beam exhausted; also 60 MJ/m2 in 1 msec)
Disadvantages and R&D needs
  Liquid metal surfaces and flows need to be stable
  Liquid metal chemistry needs to be controlled
  Temperature windows need optimization
Most of experience in fusion is with Li, but Sn and eutectics (e.g. Sn-Li) offer some promise in terms of broader temperature windows

## Slide 28: Lithium (solid and liquid) PFCs can enhance confinement
28
2-4x improvement over ITER98P(y,2)
(H-mode scaling)
H98y2 increased from 0.8 -> 1.4 (H-mode scaling)
NSTX
J.C. Schmitt et al, Phys. Plasmas 22 (2015) 056112
LTX
D.P. Boyle et al., J. Nucl. Mater. 438 (2013) S979

## Slide 29: Outline
Introduction to magnetic confinement and tokamaks
Plasma exhaust via magnetic X-point divertors
  Particle exhaust
  Momentum and power exhaust
  Recently identified challenges to attractive core-edge plasma scenarios with W walls
Types of transient events, and their impact
29

## Slide 30: What if the heat flux from the plasma is time-varying?
The heat flux from the plasma is indeed variable in time, with a ‘DC’ component and periodic eruptions
  The biggest problems are ‘disruptions’, when the plasma current and energy quenches in ~ milliseconds; ITER must either avoid disruptions or mitigate their effects!
  More periodic events include edge localized modes (ELMs), which can eject 10% of the plasma energy in ~ 0.5 msec
  Turbulence (thermodynamic) and other instabilities can regularly release up a few tenths of plasma energy rapidly
Substantial research goes into understanding and controlling transient events in fusion devices
30

## Slide 31
NSTX-U Facility Parameters
Major Radius 0.90 m
Minor Radius ≤ 0.55 m
Plasma Current ≤ 2.0 MA
Toroidal Field ≤ 1.0 T
Neutral Beam Power ≤ 12 MW
RF Heating ≤ 6 MW
Pulse Length ≤ 10 sec
NSTX was a fusion research facility at PPPL, presently undergoing a major upgrade
31

## Slide 32: ELMs are periodic eruptions in ‘H-mode’ plasmas (NSTX)
32

## Slide 33: ELMs are periodic eruptions in ‘H-mode’ plasmas (MAST)
33

## Slide 34: Solar flares are also periodic eruptions
34

## Slide 35: What Are Edge Localized Modes (ELMs)? Most likely violations of ideal or resistive MHD stability limits
Plasmas undergo a transition from low (L-mode) to high (H-mode) when enough heating power is added
The edge plasma pressure develops a stair-step or “pedestal” in H-mode
core
edge
divertor
Radius (m)
Pressure (kPa)
L-mode
H-mode
j||
SOL
SOL = Scrape-Off
Layer
35
Notes: 35
35

## Slide 36: ELMs expel plasma from the low field side, which is prone to ballooning-type pressure driven modes
Plasmas undergo a transition from low (L-mode) to high (H-mode) when enough heating power is added
The edge plasma pressure develops a stair-step or “pedestal” in H-mode
The steep edge pressure gradient and/or edge current can destabilize Edge Localized Modes (ELMs), where a portion of the pedestal pressure and energy is periodically expelled
Radius (m)
Pressure (kPa)
Pre-ELM
Post-ELM
j||
ELM
edge
divertor
SOL
SOL = Scrape-Off
Layer
36
Notes: 36
36

## Slide 37: What Are Edge Localized Modes (ELMs)?
Plasmas undergo a transition from low (L-mode) to high (H-mode) when enough heating power is added
The edge plasma pressure develops a stair-step or “pedestal” in H-mode
The steep edge pressure gradient and/or edge current can destabilize Edge Localized Modes (ELMs), where a portion of the pedestal pressure and energy is periodically expelled
Radius (m)
Pressure (kPa)
Pre-ELM
Post-ELM
j||
37
Notes: 37
37

## Slide 38: Plasma fluxes from ELMs on outer wall and divertor are 10 times higher than steady inter-ELM fluxes
ELM
edge
SOL
J.W. Ahn et. al., J. Nucl. Mater. 438 (2013) S317
SOL = Scrape-Off
Layer
38
Notes: 38
38

## Slide 39: ELM simulators used to assess ELM heating limits in ITER
Russian ELM simulator, showing damage to Tungsten surface with ITER ELM-like plasma bombardment of Tungsten
After 100 simulated 1.6 MJ ELMs, substantial tungsten melting that covers gaps between tiles
Zhitlukhin et. al. J. Nucl. Mater. 363 (2007) 301
39

## Slide 40: ELMs can be avoided or mitigated in several ways
ELMs are caused by having too much pressure and/or current near the plasma boundary
Solutions:
Trigger rapid, tiny ELMs with pellets
Apply additional 3-D fields to eliminate ELMs
  Tiny leak in magnetic bottle - pressure relief
Operate with some other instability that relieves the plasma pressure continuously – ‘quiescent’ modes
Operate far away from large, naturally occurring ELM conditions, or in tiny ELM conditions
Widen the ELM-stable operating window
  One way to do this is to change the plasma characteristics responsible for ELMs -> lithium or boron powder injection
40
Review: R. Maingi, Nucl. Fusion 54 (2014) 114016

## Slide 41: ELM mitigation via pellets and magnetic perturbations to trigger small, frequent ELMs are baseline for ITER
ITER ELM coils, 3 x 9 coils
ITER Pacing pellet trajectory schematic

## Slide 42: Acceptable ELM size in ITER depends strongly on ELM heat flux deposition region (“wetted area”)
DWELM < 0.7 MJ (0.2% Wp)
  50% of damage limit, not including fatigue
Inter-ELM heat flux width lq ~ 1/Ip
  ELM wetted area critical
A. Loarte et. al., Nucl. Fusion 54 (2014) 033007

## Slide 43: Required ELM frequency for acceptable ELMs in ITER increases with Ip
DWELM < 0.7 MJ (0.2% Wp)
  50% of damage limit, not including fatigue
Inter-ELM heat flux width lq ~ 1/Ip
  ELM wetted area critical
DWELM fELM = (0.2-0.4) PSOL
New analysis: minimum required fELM for acceptable heat flux
    (Including Be/W PFCs)
A. Loarte et. al., Nucl. Fusion 54 (2014) 033007

## Slide 44: ELM pacing and heat flux reduction with pellets shown in DIII-D, but more complex story from JET and AUG
L.R. Baylor et. al., PRL 110 (2013) 245001
0
100
200
300
400
500
600
700
0
10
20
30
40
50
60
70
Outer
Inner
Peak_IR (W/cm2)
Pellet
Natural
Pellet Frequency (Hz)
fELM * qpeak= Const
Reference
Paced
P.T. Lang et. al., Nucl. Fusion 53 (2013) 073010

## Slide 45: Impurity (Li) granules also trigger ELMs and reduce peak heat flux in DIII-D, but not in all conditions
A. Bortolon et. al., Nucl. Fusion 56 (2016) 056008
No ELM mitigation in ITER baseline
ELM mitigation in High Torque
A. Bortolon et. al., Nucl. Mater. Energy 12 (2017) 1030

## Slide 46: ELMs eliminated with either 3-D magnetic perturbations, or naturally via access to a Quiescent H-mode
46
T.E. Evans et al., Nature Phys. 2 (2006) 419
Magnetic Perturbations
D3D
A. Bortolon et al., Nucl. Fusion 56 (2016) 056008
Pellet ELM pacing
D3D
Li Pellets
no Pellets

## Slide 47: ELMs eliminated naturally via access to a Quiescent H-mode or via boron powder injection triggering quiescence
47
K.H. Burrell et al., Nucl. Fusion 53 (2013) 073038
Quiescent H-mode D3D
B powder injection EAST (May 2019)
B injection
B inj.
No B
Stored Energy [kJ]
Density [1019 m-3]
Z. Sun et al., PRL and A. Diallo et al., NF, both in preparation
B-V edge [au]

## Slide 48: ELMs eliminated by lithium wall conditioning or by operating far from instability boundaries
48
R. Maingi et al., PRL 103 (2009) 075001
Lithium conditioning NSTX
I-mode C-Mod
A.E. Hubbard et al., IAEA 2012 paper

## Slide 49: Control of plasma exhaust is an exciting fusion research area with engaging science and technology
Vibrant topic with substantial domestic and international effort
Engineering the plasma-material interface is critical to the success of fusion
Expertise needed in all areas beyond physics and NE: materials science, chemistry, large scale computing…
Early career researchers can make meaningful contributions
49
Notes: 49

## Slide 50: THANK YOU FOR YOUR ATTENDANCE
50