## Slide 1
Inertial Confinement Fusion (ICF)
as an Energy Source and for Basic Science
Maria Gatu Johnson
High-Energy-Density-Physics Division
MIT Plasma Science and Fusion Center
SULI Plasma Physics Course,
PPPL, June 15, 2017
Notes: Introduce myself
Inertial confinement fusion = laser fusion
What we see here is the inside of the target chamber on the National Ignition Facility in Livermore, California. We will get back to this later in the talk so I won’t give you any details now --- POINT OUT TARGET

## Slide 2
Maria Gatu Johnson
High-Energy-Density-Physics Division
MIT Plasma Science and Fusion Center
Inertial Confinement Fusion (ICF)
as an Energy Source and for Basic Science
SULI Plasma Physics Course,
PPPL, June 15, 2017

## Slide 3
Outline
3
Fusion Basics
The principle of Inertial Confinement Fusion (ICF)
  ICF facilities
  The OMEGA laser facility
  The Z pulsed power machine
  The National Ignition Facility (NIF)
  NIF experiments
  Status
  Engineering and scientific challenges
Basic-science experiments on OMEGA and the NIF

## Slide 4
Fusion combines light nuclei to a heavy nucleus and releases
huge amount of energy (~106× more than fossil fuel / AMU)
4
In DT fusion, ~0.4 % mass is converted to kinetic energy
D + T  4He + Neutron + Kinetic energy
Deuteron (D)
4He
Neutron
5He
Triton (T)
Fusion basics
Notes: Main laboratory fusion reaction: D+T (most easy to make happen, large energy gain)
Describe image: E=mc^2 - Einstein - Mass converted to energy

## Slide 5
Deuterium is extracted from sea water (~1 part in 5000
of the hydrogen in seawater is deuterium)
5
1 km
1 km
1 km
= Total energy of
the oil reserve
Tritium is unstable and does not exist naturally. It must be produced in a reactor via the n+6Li and n+7Li reactions
Fusion basics
Notes: Deuterium is extracted from sea water through an isotope exchange process, using e.g. the Girdler sulfide process.
Girdler-Sulfide exploits the temperature dependence of the exchange of deuterium between water and hydrogen-sulfide gas (H2S). In a typical GS heavy-water extraction tower, ordinary water is passed over perforated trays over which gas is bubbled. In the “hot section” of each tower the deuterium will migrate to the hydrogen-sulfide gas, and in the cold section, the deuterium migrates back into cold feedwater.

## Slide 6
It takes energy to overcome the Coulomb barrier.
Particles can be accelerated (Beam Fusion)
6
Coulomb
repulsion
5He
T
D
Neutron
4He
Very ineffective approach as most energy is lost to heating the cold target electrons
Fusion basics
MIT accelerator
+
+
Notes: Anne went over Coulomb repulsion earlier in the course
Particles of the same charge repel each other
To get them to fuse, we have to get them really close together
We actually do use this method to make fusion, but it will never lead to energy gain

## Slide 7
It takes energy to overcome the Coulomb barrier.
Particles can be heated (Thermonuclear Fusion)
7
If the ions are sufficiently hot (i.e. large random velocity), they can overcome the coulomb repulsion and fuse
HOT PLASMA
Coulomb
repulsion
5He
T
D
Neutron
4He
Fusion basics
+
+

## Slide 8
Fusion does not come easy! We need ~100 million Kelvin
for a significant number of fusion reactions to occur
8
Reactivity <sv> (m3/s]
10-24
10-23
10-22
10-21
1.0
10
100
Temperature, T [keV]
~100 million K
The plasma also needs to be at high enough density and confined for a long enough time…
Fusion basics
Yield = ni  nj  <v>ij  Volume  time
Notes: This is also a nice illustration of why D+T is the primary target reaction in fusion research

## Slide 9
There are three main approaches to confining a fusion plasma
9
Gravitational confinement
Magnetic confinement
Inertial confinement
Fusion basics
Notes: Gravitational confinement: Used in stars like our sun
Magnetic: you talked a lot about this earlier in the course. Use the fact that charged particles are confined in a magnetic field (spiral around magnetic field lines)
Inertial: Fuel kept together long enough by its own inertia for fusion to happen

## Slide 10
The fusion plasma conditions and confinement times
are very different for the three approaches
10
Gravitational confinement
Magnetic confinement
Inertial confinement
n ~ 1014 cm-3
tc ~ 1 s
n ~ 1026 cm-3
tc ~ 3×10-11 s
T ~ 100 million K
n ~ 1026 cm-3
tc ~ 104 years
T ~ 100 million K
T ~ 15 million K
Fusion basics

## Slide 11
Outline
11
Fusion Basics
The principle of Inertial Confinement Fusion (ICF)
  ICF facilities
  The OMEGA laser facility
  The Z pulsed power machine
  The National Ignition Facility (NIF)
  NIF experiments
  Status
  Engineering and scientific challenges
Basic-science experiments on OMEGA and the NIF

## Slide 12
ICF uses the inertia of a dense shell to confine the plasma before it blows apart under its own pressure
12
Principle of ICF
The confinement time (tc) can be
expressed in terms of the sound speed cs:
High-density DT shell
DT gas core
R
ρ
Local confinement time:
Rarefaction propagates into and decompresses the
assembled mass at the sound speed cs
M. Rosen, Phys. Plasmas 6, 1690 (1999)
Mass average:
Notes: The confinement time is the volume over the rate of change of the volume

## Slide 13
“Areal density” R is a key performance parameter in ICF
Principle of ICF
The confinement parameter (ntc) can now be expressed as:
Notes: number density n=density/mass
rhoR is a measurement of the quality of the confinement – a major figure of merit for an ICF implosion

## Slide 14
4He
n
Ignition occurs when fusion energy carried/deposited
by the 4He ions balances the energy losses
14
The ignition criterion for ICF is ~20 times higher than that of MCF due to inefficiencies in assembling the fuel
Energy losses:
Radiation
Thermal conduction
PdV expansion
Principle of ICF
at ~5 keV
4He ion energy
= 3.6 MeV
Fusion reactivity
Energy confinement
Ideal gas law
Notes: START WITH THE IMAGE: Describe the idea. Reactions happen in the hot core, alpha particle reaction products deposit their energy in the fuel, making more fuel hot to generate more reactions
Plasma pressure <p>=niTe+neTe  p~2nT
Ideal gas law pV=NkT=nVkT

## Slide 15
The fuel burn fraction (f) depends on R
15
Principle of ICF
Fusion burn rate
Integrate over confinement time
Burn fraction
M. Rosen, Phys. Plasmas 6, 1690 (1999)
Notes: Separation of variables  dn/n^2 = dt/2*<sv>
n=2 x nT
This works because dnT/dt=dn/2dt

## Slide 16
A high ρR is required for high ntc values and for a significant fraction of the fuel to burn before it disassembles
16
If fb = 25% (required for ignition) → rRDT ~ 2 g/cm2
ρDT, solid = 0.25 g/cm3
→
For ignition, we need a DT-fuel mass (mDT) of about
Principle of ICF
Notes: Assume we work with nominal solid DT density, how much mass is required for ignition?

## Slide 17
So what’s the problem? Why can we not work with
0.5 kg of DT fuel in a fusion reactor?
17
Principle of ICF
Burn fraction
DT mass

## Slide 18
Solution: compress the ICF capsule to increase DT
18
Compression
Principle of ICF
DT
gas
R
ρDT
CH-ablator
rDT = 0.25 g/cm3
R ~ 1100 mm
rRDT ~ 0.03 g/cm2
High-density DT shell
DT gas core
R
ρDT
rDT ~ 700 g/cm3
R ~ 30 mm
rRDT ~ 2 g/cm2

## Slide 19
Spherical compression is most efficient
Principle of ICF
Must exploit R3 compression with spheres – R2 or R1 scaling with cylindrical or planar compression is not adequate
In practice, a hollow shell has more surface area and is easier to push with a given pressure than a solid sphere of the same mass
Goal: Convert shell kinetic energy to compression energy

## Slide 20
The capsule must be compressed ~35× (R/R < 1%)
to achieve the right conditions (Basketball → green pea)
20
~35×
Green pea
Principle of ICF

## Slide 21
ICF implosion timeline
21
1. Laser irradiates and heats the surface,
increasing the pressure
4. “Bang time” is the time of peak nuclear production
n
4He
2. Ablation of the surface material
accelerates the capsule inwards
3. Temperature and density
increase as fuel compresses
~20ns
~30 ps
Principle of ICF
Notes: 1. Radiation energy is absorbed near the outer surface of the capsule
2. Energy deposition causes material to ablate rapidly; ablation produces implosion
3. Fuel is compressed and stagnates around a low-density central hot spot, where shock convergence and compression energy heat the fuel and spark fusion reactions
4. Fusion products deposit energy throughout the bulk of the compressed fuel, igniting the capsule
“In step 1, laser energy is (collisionally) absorbed by electrons as the laser propagates up to and back from the critical surface.”
“That energy is conducted to the ablation surface at the edge of the shell, where material is ablated.”
“That ablation pressure drives the shell inward, assembling the compressed fuel around a low-density hot spot.”
“At that point, the energy imparted by the compression and shock convergence sparks fusion reactions.”
“Provided the compression is good enough, fusion product energy will be deposited in the bulk of the fuel, igniting a burn wave that propagates throughout the fuel.

## Slide 22
The most efficient compression is isentropic
Principle of ICF
Minimize Entropy Generation
Minimize Work Needed to Compress
Change in Density
Change in Pressure
Isentropic Compression
Shock Compression
1
10
10
100
From thermodynamics:
Notes: U = internal/thermal energy
T = temperature
S = entropy
P = pressure
V = volume
First law of thermodynamics: The change in energy of a system is equal to the difference between the heat added to the system and the work done by the system, E=Q-W (E=U if potential and kinetic energy can be neglected.)
Second law of thermodynamics: There exists for every system in equilibrium a property called entropy, which is a thermodynamic property of a system. For a reversible process, changes in this property are given by dS = dQ/T.

## Slide 23
But ICF doesn’t have ideal compression
Principle of ICF
Fast time-scales lead to shocks, which have compression limits
  Solution: Multiple timed shocks to keep implosion as efficient as possible. A “shaped” pulse.
For this reason, shaped laser pulse are used

## Slide 24
There are two different laser-drive schemes
24
Laser directly
irradiates capsule
Direct drive
Indirect drive
Laser produces x-rays inside a hohlraum, which irradiate the capsule
Principle of ICF
The two approaches trade efficiency for uniformity
8% efficiency
4% efficiency

## Slide 25
Direct Drive
Indirect Drive
High-Z Hohlraum
Laser Beams
DT-filled
Capsule
A NIF Capsule
(2 mm diam.)
X rays
Capsule
Magnetic Drive
In addition, there is also a magnetic drive scheme, for a total of three primary approaches to ICF
Principle of ICF

## Slide 26
Want to know more? A good book on the basics of ICF is “The Physics of Inertial Fusion” by Atzeni and Meyer-Ter-Vehn
Principle of ICF

## Slide 27
Fusion Basics
The principle of Inertial Confinement Fusion (ICF)
  ICF facilities
  The OMEGA laser facility
  The Z pulsed power machine
  The National Ignition Facility (NIF)
  NIF experiments
  Status
  Engineering and scientific challenges
Basic-science experiments on OMEGA and the NIF
Outline
27

## Slide 28
The OMEGA laser facility at University of Rochester
uses the direct-drive approach
28
ICF facilities
~70 m
Direct-drive implosion
Capsule
60 laser beams delivering 30 kJ
Notes: Go over each image in turn, starting from the facility overview (upper right)

## Slide 29
The goal of direct-drive experiments at OMEGA is to demonstrate ignition feasibility for indirect drive
ICF facilities
60 kJ energy available on OMEGA.
If laser energy was scaled up to 2 MJ, would the direct drive implosions ignite?
Currently trying to demonstrate this by reaching 100 Gbar pressure. 50 Gbar demonstrated
S. Regan, Phys. Rev. Lett. 117, 025001 (2016)

## Slide 30
80 TW
33 Meter diameter
26 MA
22 MJ Stored Energy
Magnetic drive ICF is being pursued at the Z pulsed power facility at Sandia National Labs, NM
Principle of ICF

## Slide 31
Goal: Demonstrate ~100kJ DT eq fusion yield
In magnetic drive ICF, an axial current creates a JxB force that is used to implode a gas-filled, pre-magnetized target
Principle of ICF
Notes: An axial current creates a JxB force that is used to implode a gas-filled, pre-magnetized target. Near the start of the implosion, the fuel is heated by the laser. The liner compresses and further heats the fuel to fusion-relevant conditions at stagnation.

## Slide 32: Inertial confinement fusion (ICF) seeks to use lasers or x-rays to compress and ignite a capsule of DT fuel
The National Ignition Facility (NIF) is a three football stadium-sized laser, which uses the indirect-drive approach
10 m diameter chamber
192 beams
Temperature > 100 MK
Density > 1000 solid
Pressure > 1011 atm
ICF facilities

## Slide 33
NIF delivers about 1.8 MJ of laser energy
to a cm-scaled hohlraum
33
~200 m
~1 cm
W
ICF facilities

## Slide 34
Movie time!
ICF facilities
https://lasers.llnl.gov/about/how-nif-works

## Slide 35
NIF was inaugurated in 2009 and is now being
used for ignition and basic-science experiments
35
ICF facilities

## Slide 36
NIF also played an important role
in the movie Star Trek – Into Darkness
36
Courtesy of Scott Chambliss, Paramount Pictures and Bad Robot Productions.
ICF facilities

## Slide 37
The ICF targets are really small!
ICF facilities

## Slide 38
Outline
38
Fusion Basics
The principle of Inertial Confinement Fusion (ICF)
  ICF facilities
  The OMEGA laser facility
  The Z pulsed power machine
  The National Ignition Facility (NIF)
  NIF experiments
  Status
  Engineering and scientific challenges
Basic-science experiments on OMEGA and the NIF

## Slide 39
Many institutions are involved in the experiments on the NIF
39
NIF experiments
LLNL
– FABS, NBI
– Dante I & II
– VISAR
– DISC
– RAGS
– hGXI
– ARIANE
– DIXI
– NAD
AWE
– FFLEX
LANL
– GXD
–  burn
– Rad. Chem. II
– N imaging
SNL
– SPIDER
– DISC
– NAD (Cu)
– NToF
– RAGS
NSTec
– Calibration
– NToF
LBNL
– Calibration
– Rad. Chem.
CEA
– N imaging
MIT
– MRS
– WRF
– pTOF
LLE
– NToF
– 4 fidu system
– MRS, NADS
– SPBT
– HEXRS
GA
– NToF
– Capsules

## Slide 40
A DT implosion is diagnosed with optical, x-ray
and nuclear techniques on the NIF
40
Fusion yield:
From DT neutrons
Fuel Ion temperature
From DT-neutron spectrum
Areal density (rR)
From scattered DT neutrons
Implosion and burn history
X-ray and neutron production
Implosion shape
From x-ray and neutron images
NIF experiments

## Slide 41
A DT implosion is diagnosed with optical, x-ray
and nuclear techniques on the NIF
41
Fusion yield:
From DT neutrons
Fuel Ion temperature
From DT-neutron spectrum
Areal density (rR)
From scattered DT neutrons
Implosion and burn history
X-ray and neutron production
Implosion shape
From x-ray and neutron images
NIF experiments

## Slide 42
The 4He ions (or alphas) are confined and heat
the DT fuel, while the neutrons escape
42
The conditions in the implosion can be diagnosed by measuring the spectrum of the emitted neutrons
D + T  4He + n + 17.6 MeV
4He
n
NIF experiments

## Slide 43
The neutron spectrum provides info on ρR, Ti and Yn – Essential info for assessing the implosion performance
43
n'
T
n
n
n'
D
Yn
n
n'
Yn’
NIF experiments

## Slide 44
44
NIF target bay
20m-nTOF
(alcove)
20m-nTOF
(south pole)
20m-nTOF
(equator)
Several neutron spectrometers are fielded
at various locations on the NIF
NIF experiments
MRS
NITOF
This provides good implosion coverage for reliable measurements of Yn, Ti, R and R asymmetries

## Slide 45
MIT built the Magnetic Recoil Spectrometer (MRS), which
measures the neutron spectrum
45
26 cm
570 cm
CR-39
CD-foil
3-18 MeV (d)
Implosion
d
n
MRS
NIF experiments

## Slide 46
Yield and R derived from neutron data determine
implosion performance; significant progress has been made
46
NIF experiments
0.4
1.4
0.6
0.8
1.0
1.2
Fuel R [g/cm2]
Neutron yield
Yield magnification from alpha heating
Alpha-heating
Y/Yno a
Burn

## Slide 47
Big news (Nature, Feb 2014): NIF reached “scientific breakeven”!!
NIF experiments

## Slide 48
“Scientific breakeven” means that more energy was generated than was coupled into the DT FUEL
NIF experiments
NIF was built to achieve ignition – working definition of ignition is yield higher than input laser energy (>1MJ)
Notes: We are still ~100 times below the end goal

## Slide 49
“Energy generated” is simply calculated from the measured neutron yield
NIF experiments
Efusion=YDT17.6 MeV
Total energy release in each D+T reaction
Measured by neutron diagnostics!

## Slide 50
“Energy coupled to the fuel” is calculated based on measured parameters
NIF experiments
Total energy coupled
Energy in hot spot and fuel at time of implosion
Energy lost at time of implosion
Energy deposited through fusion burn at time of implosion
4He
n
hot spot
fuel
All quantities are calculated from:
hot spot radius/shape, burn duration (x-rays)
yield, downscattered neutrons, ion temperature (neutrons)

## Slide 51
Capacitors ~ 400MJ
However, potential gain is very high (up to ~10s MJ, fuel gain ~103)
Energy coupling in inertial fusion is very inefficient - there are still many steps remaining before net energy gain is achieved
NIF experiments

## Slide 52
More progress has been made since Nature publication – the fuel now has gain ~2
NIF experiments
In Nature
New
~12kJ heating
fuel
~27kJ fusion energy
1.8MJ
laser …

## Slide 53
What are the challenges? Ignition designs must simultaneously manage instability growth, symmetry, fuel entropy, and laser-plasma interactions
Manage LPI
Needed for
high V and rR
Manage fuel entropy
Needed for high rR
Manage hotspot
and shell shape
Compression
hot-spot
shell
flows?
Needed for high hotspot coupling
Manage
RT growth
Ignition requires:
Good hotspot coupling
High compression
High implosion velocity

## Slide 54
There is growing evidence that NIF implosions are highly 3D in nature at burn
D.S. Clark et al., Phys. Plasmas 22, 022703 (2015)
Cartoon concept:
Reality?
DT gas
Ablator
DT ice
Notes: Evidence: FNADs, X-ray images, Neutron images, Dsr asymmetry and magnitude, Performance, Tion
Hohlraum drive asymmetry and capsule support tent believed to be the primary causes of the asymmetries

## Slide 55
Progress comes from “taking a step back” to improve understanding – more systematic approach
55
NIF experiments
0.4
1.4
0.6
0.8
1.0
1.2
Fuel R [g/cm2]
Neutron yield
Alpha-heating
Y/Yno a
Burn
We now understand that hydrodynamic instability growth limited the performance of these implosions
“Low foot”
“High foot”

## Slide 56
The difference between the high and low foot experiments are in how isentropically they are compressed
NIF experiments
Low foot
a ~ 1.5
High foot
a ~ 2.5
Low foot
Low foot

## Slide 57
Hydrodynamic instability leads to mix of highly radiating material into the hotspot, which quenches the burn
NIF experiments
Impurities in target act as seeds for instability growth:

## Slide 58
The “tent” used to hold the capsule in the hohlraum is believed to seed instability and break the symmetry
NIF experiments
110-nm tent
45-nm tent
Optical Depth Image showing tent “scar”
Hammel
15°
Stadermann, et al.
Hydra simulation
Expt

## Slide 59
The fill tube used to add DT gas to the capsule is also a possible source of instability growth
59
NIF experiments

## Slide 60
NIF experiments
Simulations are useful to help peer into details of the experiment otherwise inaccessible
D. Clark –
3D Simulation of low foot N120405
C. Weber –
Postprocessed movie
3D HYDRA simulation of final stagnation phase
Simulations predict perturbations will grow and severely damage the implosion at stagnation
Density
Temperature

## Slide 61
Lo-Foot vs Hi-Foot Growth factor at 650 µm
Chart: Mode Number
| 30 | 60 | 90 | 120 | 160
LowFoot Data | 240 | 1025 | 896 | 293.4 | 99.18
HighFoot Data | 115 | 221 | 45 | 0 | -62
LowFoot simulation | 76.1933 | 506.268 | 820.1542 | 797.3721 | 556.8948 | 291.1041 | 105.5569 | 17.7194 | -9.0495
HighFoot simulation | 35.4388 | 198.7102 | 234.149 | 162.0058 | 67.0805 | 17.7194 | 2.2782 | 4.8728 | -9.2394 | 1.5188
Zero Axis | 0 | 0
Simulation
Low foot
Ripple target
X-ray snapshots
650 µm
High foot
time
The recent, lower convergence implosions are more resilient to small target imperfections due to lower growth rates
NIF experiments
Recent implosions have had low mix because they converged less
Now we want to go back to higher convergence without introducing mix

## Slide 62
First test: Push these low-convergence implosions to higher velocity using thinner ablator layers
NIF experiments
High foot
(no coast)
195µm
DT Yield vs. Laser Energy
High foot
(coast)
DU
175µm
165µm
?
?

## Slide 63
Bremsstrahlung ~ Z2
High-foot:
mix free at high velocity
Mix vs. implosion Velocity
This was demonstrated to work well – implosions did not mix even at very high velocity
NIF experiments
Low-foot:
High mix at intermediate velocity

## Slide 64
Another outstanding question concerns inefficiencies in assembling the fuel
NIF experiments
Non-uniformities in hotspot
 pdV work lost to setting fuel in motion
Non-uniformities in fuel layer
 less efficient inertial confinement
Notes: Asymmetries can be on different scale:
-small scale asymmetries are highly related to mix.
-Large scale asymmetries have to do with how efficiently the fuel is assembled
We need to compress symmetrically in order to effectively convert kinetic energy to thermal energy in the hot spot
Nature article: Because most of the quantities associated with inertially confined fusion that we seek to improve to achieve ignition scale as some positive power of stagnation pressure, near-term efforts focus on increasing the implosion speed and controlling the hot-spot shape with the present fuel adiabat.

## Slide 65
X-ray and neutron measurements of hot-spot shape indicate significant hot-spot asymmetry
NIF experiments
Time-integrated x-ray emission (equatorial view)
Time-integrated x-ray emission (polar view)
Time integrated neutron (equatorial view)
13-17 MeV
6-12 MeV
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-100
-50
100
50
0
-100
-50
100
50
0
-100
-50
100
50
0
-100
-50
100
50
0
-100
-50
100
50
0
-100
-50
100
50
0
-100
-50
100
50
0
-100
-50
100
50
0
100
80
60
40
20
100
40
20
60
80
-50
50
0
-60
60
0
13-17 MeV
6-12 MeV
13-17 MeV
6-12 MeV
13-17 MeV
6-12 MeV
13-17 MeV
6-12 MeV
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0
-50
50
0

## Slide 66
Neutron spectrometry measurements indicate directional motion of the hotspot during burn
NIF experiments
Directional or turbulent motion “steals” kinetic energy from the pdV work on the hotspot and must be minimized
Spec E
DT: 4 ± 25 km/s
DD: -4 ± 15 km/s
Spec A
DT: -9 ± 25 km/s
DD: -39 ± 15 km/s
Spec SP
DT: -20 ± 25 km/s
DD:-37 ± 15 km/s
NITOF
DT: -3 ± 4 km/s
Notes: Velocity is inferred from shifts in the peak location of the neutron spectrum
Velocities shown in this example (measured on a recent shot) are pretty low, but this is not always the case
Clear illustration of how we need to compress symmetrically in order to effectively convert kinetic energy to thermal energy in the hot spot

## Slide 67
Neutron spectrometry measurements indicate substantial, systematic low-mode dense fuel ρR asymmetry
67
MRS
Spec-E
Spec-A
10-12 MeV
10-12 MeV
NIF experiments
Notes: need to compress symmetrically in order to effectively convert kinetic energy to thermal energy in the hot spot
Confinement is never better than the lowest rhoR region

## Slide 68
Directional neutron yield measurements also indicate substantial dense fuel R asymmetry
NIF experiments
-10% 0% +10%
Fuel maps from neutron activation
N141123
N150121
N150115
N150318
Purposely asymmetrically driven

## Slide 69
So, we are still struggling with symmetry. Current path forward:
NIF experiments
Control asymmetry seeding due to engineering features
Improve understanding of hohlraum physics to control asymmetry seeding due to non-uniform drive

## Slide 70
NIF experiments
30 µm FT @ 65 Hz
measurements from GA
capsule
10 µm fill-tube
Engineering features: The best solution would be to eliminate the tent altogether but there are challenges
30 µm free-standing fill-tube vibration test

## Slide 71
A better understanding of and ability to control laser-plasma interactions in the hohlraum is essential
NIF experiments
Cross-beam energy transfer
Hot electron preheat
X-rays, M-band
SBS-outers
SRS and SBS-inners
The hohlraum drive is not yet predictable
Hohlraum physics may impact implosion symmetry
A ~15% loss of drive energy cannot be accounted for in simulations

## Slide 72
The hohlraum must provide a symmetric x-ray drive to enable efficient transfer of the drive to the hotspot
Laser "Pulse-shape"
Plastic Ablator
Gold hohlraum wall
Helium gas
Inner cone beams
Laser entrance hole (LEH)
~ 1cm
HYDRA Simulation Jose Milovich

## Slide 73
Gas-filled
Near vac
One research direction: low-gas fill hohlraums  better predictability
Other potential options: Different hohlraum shape, e.g., different case-to-capsule ratio, rugby
NIF experiments
A better understanding of and ability to control laser-plasma interactions in the hohlraum is essential

## Slide 74
MIT has been heavily involved in the NIF program
74
NIF experiments
Former NIF director
Ed Moses
Exp. director
Joe Kilkenny
Hans
Alex
Mike
Maria
Dan

## Slide 75
1st PhD thesis based on NIF data was presented
by former MIT graduate student Dan Casey
75
Alex
Dan
LLNL director Parney
Albright
NIF experiments

## Slide 76
Outline
76
Fusion Basics
The principle of Inertial Confinement Fusion (ICF)
  ICF facilities
  The OMEGA laser facility
  The Z pulsed power machine
  The National Ignition Facility (NIF)
  NIF experiments
  Status
  Engineering and scientific challenges
Basic-science experiments on OMEGA and the NIF

## Slide 77: High-Energy-Density Physics (HEDP) involves studies of matter under extreme states of pressure (~ 1 Mbar to ~ 1000 Gbar)
Solar core ~ 250 Gbar
Igniting ICF implosion ~ 300 Gbar
Earth’s core ~ 3 Mbar
We exploit the extreme conditions
at the OMEGA and NIF laser facilities and the Z pulsed power machine
for astrophysical, nuclear, ICF and other HEDP experiments
Basic science experiments
Notes: These states are created in the lab using high-power lasers
Relevant physics scenarios:
  Interior of planets
  Interior of stars
  Fusion
  Collisional/collisionless shocks

## Slide 78
The ICF platform lends itself to a wide range of basic science experiments
Basic science experiments
Plasma/WDM stopping power
Collisionless shocks
Astrophysical jets
Magnetic reconnection
Nuclear astrophysics
.
.
x
x
B
Side-on
Jet
Driven laser beams
Jet
V-shaped CH target
Plasma plume
1.
2.
3.
4.
5.

## Slide 79
MIT’s own OMEGA experiments include basic science as well as ICF programmatic-relevant work
Basic science experiments
Recent examples include:
Kinetic effects in ICF plasmas
Stopping power in ICF and in Warm Dense Matter
Stellar and Big-Bang Nucleosynthesis
Basic nuclear physics
Astrophysical Jets
Fields in hohlraums
Magnetic reconnection
Rayleigh-Taylor instabilities

## Slide 80
Proton source
Proton detector
Subject plasma
3 and 15 MeV protons
Spatial resolution: ~ 40 mm (FWHM)
Energy resolution: ~ 3%
Temporal resolution: ~ 80 ps
Initial capsule
Compressed
capsule
Thin SiO2
D3He
gas
15 atm
D3He
D + 3He  p(14.7 MeV) + 
D + D  p(3.0 MeV) + T
D + D  n + 3He
C. K. Li et al., Phy .Rev. Lett. (2006)
C. K. Li et al., Rev.Sci.Instrum (2006)
F. Seguin et al., Rev.Sci.Instrum (2003)
MIT has developed a D3He monoenergetic particle platform for radiography of HEDP experiments

## Slide 81
Phenomena investigated with monoenergetic proton radiography at OMEGA include:
  Laser-foil interactions
  Magnetic reconnection
  Magnetic flux compression
  RT instability
  Weibel instability
  ICF capsule implosions
  ICF hohlraums
  Charged-particle stopping
Proton source
Proton detector
Subject plasma
3 and 15 MeV protons
Fast-ignition capsule
Laser-foil plasma bubble
ICF hohlraum
MIT has developed a D3He monoenergetic particle platform for radiography of HEDP experiments

## Slide 82
Thank you for your attention!
82

## Slide 83
Laser Driver
Laser Light
Target Injection
Lithium Blanket
Heat Transfer
Target Fabrication
Tritium Fuel Cycle
Heat Exchg.
Turbine
12 meters
Concept for an ICF power plant