## Slide 1
Single Particle Motion
Presented by
Cami Collins
at the
SULI Introductory Course in Plasma Physics
Princeton Plasma Physics Laboratory
June 10, 2019

## Slide 2: My path in plasma physics
🇫🇮

## Slide 3
plasma physics
turbulence
transport
I want fusion energy to work.
But what does that mean?
stability

## Slide 4
plasma physics
computer science
steady state
ELM controlled
disruption mitigation
turbulence
transport
high confinement
I want fusion energy to work.
But what does that mean?
stability
efficient current drive
control
high bootstrap current
shaping
high beta
dissipative divertor
engineering

## Slide 5
engineering
plasma physics
computer science
materials science
tritium breeding
steady state
ELM controlled
disruption mitigation
turbulence
transport
high confinement
alpha heating
I want fusion energy to work.
But what does that mean?
stability
efficient current drive
control
power handling
high bootstrap current
shaping
high beta
dissipative divertor

## Slide 6
engineering
plasma physics
computer science
materials science
tritium breeding
steady state
ELM controlled
disruption mitigation
turbulence
transport
nuclear materials
net electricity
metal walls, liquid walls?
heat extraction
high confinement
alpha heating
I want fusion energy to work.
But what does that mean?
licensing
stability
efficient current drive
control
power handling
high bootstrap current
shaping
high beta
dissipative divertor

## Slide 7
engineering
plasma physics
computer science
materials science
political science?
tritium breeding
steady state
ELM controlled
disruption mitigation
turbulence
transport
nuclear materials
net electricity
metal walls, liquid walls?
heat extraction
high confinement
alpha heating
I want fusion energy to work.
But what does that mean?
licensing
stability
efficient current drive
control
power handling
high bootstrap current
shaping
high beta
dissipative divertor
social science?
$
$
$
$
$

## Slide 8
Deuterium
~0.01 MeV
Helium
3.5 MeV
Neutron
14.1 MeV
Tritium
~0.01 MeV
Sustained fusion reactions require enough particles (density) that are energetic enough (temperature) and collide often enough (confinement time).
Plasma Physics is the Basis for Fusion Research

## Slide 9
Deuterium
~0.01 MeV
Helium
3.5 MeV
Neutron
14.1 MeV
Tritium
~0.01 MeV
Sustained fusion reactions require enough particles (density) that are energetic enough (temperature) and collide often enough (confinement time).
The fusion triple product is the figure of merit:
T~100-200 million K
n~2-3x1020 ions/m3
τ ~1-2 s
D & T is a plasma at these temperatures
Plasma Physics is the Basis for Fusion Research

## Slide 10
Typical velocity of a 100 million K ion:
Even with ~1020 ions/m3 , the ion would travel ~10 km before colliding with another
It would be crazy to build a fusion reactor that big!
We can understand a lot about how fusion devices confine plasma by studying single particle motion.
The trick: use magnetic fields
charged particle
magnetic field line
with magnetic field
no magnetic field

## Slide 11: Outline
Gyromotion about a guiding center
Forces can cause guiding center drift
Real life consequences:
  Why do tokamaks have helical B fields?
  What is a banana orbit?
  Why are instabilities like Alfvén Eigenmodes bad for fusion?
NRL Plasma Formulary
  www.nrl.navy.mil/ppd/content/nrl-plasma-formulary
Introduction to Plasma Physics and Controlled Fusion by F. Chen
References

## Slide 12: Charged Particles Feel The (Lorentz) Force
A particle with charge (q) moving with velocity (v) in the presence of electric and magnetic fields will experience a force:
We know from Newton’s second law of motion that force causes acceleration:
A charged particle
moving perpendicular to
the magnetic field feels a force

## Slide 13: How Does a Charged Particle Move in a Magnetic Field?
Consider the motion of a particle in a constant, uniform B field
y
x
+
Then
So we can write

## Slide 14
y
x
+
Let’s break this into components:
Goal: Solve the Equations of Motion for a Charged Particle In A Magnetic Field
The ‘dot’ represents
Particles move freely along the field line
Matching components:

## Slide 15
Take Another Time Derivative & Substitute to Obtain Differential Equations For Each Spatial Coordinate
Rewriting, we get
These may remind you of the equations for a simple harmonic oscillator

## Slide 16
Solve the Differential Equations
These differential equations can be solved using sines and cosines:
the magnitude of the initial velocity perpendicular to B
an arbitrary phase to match the initial velocity conditions
account for positive or negative q

## Slide 17
Integrating, we obtain
Larmor radius
Cyclotron frequency
Charged particles undergo circular orbits about a guiding center
The Result: Circular Motion About A Guiding Center

## Slide 18
Let’s take and
Gyromotion of a Charged Particle In A Magnetic Field
y
x
+
For a positively charged particle:
1. At ,

## Slide 19
Let’s take and
Gyromotion of a Charged Particle In A Magnetic Field
For a positively charged particle:
1. At ,
2. At ,
y
x
+

## Slide 20
Let’s take and
Gyromotion of a Charged Particle In A Magnetic Field
For a positively charged particle:
1. At ,
2. At ,
y
x
+

## Slide 21
Let’s take and
y
x
Gyromotion of a Charged Particle In A Magnetic Field
For a negatively charged particle:
1. At ,
-

## Slide 22
Let’s take and
y
x
Gyromotion of a Charged Particle In A Magnetic Field
For a negatively charged particle:
1. At ,
2. At ,
-

## Slide 23
Let’s take and
y
x
Gyromotion of a Charged Particle In A Magnetic Field
For a negatively charged particle:
1. At ,
2. At ,
-

## Slide 24
y
x
Gyromotion of Ions vs. Electrons
+
Ions generally have a much larger Larmor radius than electrons
The direction of gyromotion depends on the sign of the charge
-
In ITER, a typical deuterium ion
with Ti=10 keV and B=5 Tesla would have
An electron with Te=10 keV and B=5 Tesla has
(60 times smaller)

## Slide 25
Magnetic Confinement Devices Should Be Much Larger Than the Larmor Radius
Particles are confined perpendicular to the applied magnetic field
Single Magnetic Field Line
Image credit: http://iter.rma.ac.be/en/img/MagneticConfinement.jpg
Tokamak approach: parallel confinement is achieved through toroidal geometry

## Slide 26
Magnetic Mirrors
Result:
gyromotion + mirror force in the direction
The Br ends up causing additional acceleration in the z direction:
The magnetic moment is
mirror force

## Slide 27
Magnetic Moment Is Conserved
The magnetic moment is a constant of motion
s is the coordinate along the field line
We can write
this is
Then
We also have conservation of energy:
this is

## Slide 28
1. As the particle moves to stronger B, must increase.
2. Since energy is conserved, must decrease.
3. If B is strong enough, and the particle is reflected.
More Insight Into Magnetic Mirrors
The particle is reflected when

## Slide 29
Magnetic Mirror Confinement In Action
Charged particles can be trapped by Earth’s magnetic field
Multicusp Confinement Devices
Early Fusion Experiments
Ex: Tandem Mirror Experiment (LLNL,1980’s) and other variants (Polywell devices)
Particles with enough v|| can still escape

## Slide 30
Time-varying Electric and Magnetic Fields Can Be Used To Accelerate & Heat Particles
A high frequency electro-magnetic field can be used to accelerate electrons or ions.
y
x
-

## Slide 31
y
x
-
A high frequency electro-magnetic field can be used to accelerate electrons or ions.
Particle gains energy as the applied electric field component oscillates at the cyclotron frequency (“in-phase” with the gyro-orbit).
Cyclotron frequency
Time-varying Electric and Magnetic Fields Can Be Used To Accelerate & Heat Particles
The fluctuating accelerates the electron in the +x direction
Notes: The transverse electric field oscillates at the cyclotron frequency. The particle velocity changes direction every half period, but so does the applied electric field. SO they remain in phase with each other. Energy is transferred to the charged particle, and the orbit will spiral outward with larger and larger rL.

## Slide 32
y
x
-
A high frequency electro-magnetic field can be used to accelerate electrons or ions.
Particle gains energy as the applied electric field component oscillates at the cyclotron frequency (“in-phase” with the gyro-orbit).
Cyclotron frequency
Time-varying Electric and Magnetic Fields Can Be Used To Accelerate & Heat Particles
Now accelerates the electron in the -x direction

## Slide 33
y
x
-
A high frequency electro-magnetic field can be used to accelerate electrons or ions.
Particle gains energy as the applied electric field component oscillates at the cyclotron frequency (“in-phase” with the gyro-orbit).
Cyclotron frequency
Time-varying Electric and Magnetic Fields Can Be Used To Accelerate & Heat Particles

## Slide 34
y
x
-
A high frequency electro-magnetic field can be used to accelerate electrons or ions.
Particle gains energy as the applied electric field component oscillates at the cyclotron frequency (“in-phase” with the gyro-orbit).
Ex: For an electron, what B corresponds to 2.45 Ghz (microwave oven frequency)?
The Cyclotron Frequency is Important for
Cyclotron Resonance Heating
Cyclotron frequency

## Slide 35
Electron Cyclotron Heating In A Plasma Experiment at UW-Madison
(2.45 GHz, B=875 Gauss)
Example of Cyclotron Heating in Action
In the DIII-D tokamak, use 110 GHz second harmonic heating (B~2 Tesla)

## Slide 36
Other Practical Applications: EM Emission from Charged Particle Acceleration
Electron cyclotron emission (measure Te profiles) Produced by acceleration of gyrating charged particle EM radiation emitted at discrete frequencies:
-
B
Detected radiated power is proportional to Te:
+
-
Bremsstrahlung emission Produced by deceleration of deflected charged particle
Radiated power depends on ne, Te, charge state Zeff
(can be used to measure Zeff)

## Slide 37
y
x
+
Next Simplest Case to Analyze: Constant, Uniform Electric Field Perpendicular to Magnetic Field

## Slide 38
y
x
+
Accelerates due to E
Faster velocity increases vxB
Next Simplest Case to Analyze: Constant, Uniform Electric Field Perpendicular to Magnetic Field

## Slide 39
y
x
+
Faster velocity increases vxB
Decelerates
Next Simplest Case to Analyze: Constant, Uniform Electric Field Perpendicular to Magnetic Field
Accelerates due to E

## Slide 40
y
x
+
Next Simplest Case to Analyze: Constant, Uniform Electric Field Perpendicular to Magnetic Field
Faster velocity increases vxB
Decelerates
Accelerates due to E

## Slide 41
Next Simplest Case to Analyze: Constant, Uniform Electric Field Perpendicular to Magnetic Field
y
x
+
Ion guiding center drifts in the direction

## Slide 42
Guiding Center Drift Due to E x B
y
x
-
The ExB drift can be written more generally as
ExB drift is independent of charge and mass
Both electrons and ions move together
Electron guiding center also drifts in the direction

## Slide 43
Other Forces Can Cause Guiding Center Drift
Any force perpendicular to B can cause particles to drift
Drift due to force:
Examples of forces:
gravity
centrifugal
Rc
Bend the magnetic field into a donut shape
No end losses because the field lines go around and close on themselves
BUT a particle following a toroidal magnetic field would experience Fcf

## Slide 44
A particle moving along a curved field line will drift up or down, depending on the sign of the charge
The outward centrifugal force causes curvature drift
z
Btoroidal
Rc
Curvature Drift Due to Bending Field Lines

## Slide 45
Spatially Varying Magnetic Field Strength Also Causes Drift

## Slide 46
+
The gyro-radius will be larger where the field is weaker and smaller where the field is stronger
Spatially Varying Magnetic Field Strength Also Causes Drift

## Slide 47
-
+
The gyro-radius will be larger where the field is weaker and smaller where the field is stronger
The resulting drift velocity is described by:
Spatially Varying Magnetic Field Strength Also Causes Drift

## Slide 48
What Happens To Charged Particles In A Purely Toroidal Magnetic Field?
Ion
drift
+
+
+
+
Electron
drift
-
-
-
-
Btoroidal
Charged particles in a curved magnetic field will experience both ∇B and curvature drift: these effects add
z
ɸ

## Slide 49
Charged Particles Will Drift Outward
Ion
drift
Electron
drift
E
+
+
+
-
-
-
+
-
Btoroidal
This means that no matter what, particles in a torus with a purely toroidal field will drift radially out and hit the walls.
Charged particles in a curved magnetic field will experience both ∇B and curvature drift
z
ɸ

## Slide 50
Tokamak Solution: Add Poloidal Magnetic Field
Iplasma
Bpoloidal
Toroidal: long way around
Poloidal: short way around
1. Use external coils to apply a toroidal magnetic field
2. Drive toroidal current in the plasma to generate a poloidal magnetic field
Btoroidal
z
ɸ
The resulting helical magnetic field is much better at confining charged particles.
The challenge: how to drive current in plasma in steady state while keeping the plasma stable and free of disruptions?

## Slide 51
z
ɸ
R
There Are Two Main Classes of Particle Orbits In Tokamaks
Passing
Bp
Bt
Particles with sufficient v||will follow the helical magnetic field around the torus
z
ɸ
R
Trapped
Bp
Bt
Particles with lower v|| are reflected as they encounter stronger B and therefore execute “banana” orbits as they precess around the torus B

## Slide 52
Image credit: euro-fusion.org
Banana Orbits
Particles that don’t have enough v|| are reflected by the mirror force at the high field side of the tokamak
Trapped particles won’t hit the wall if the banana orbit width Δr is small enough

## Slide 53
Image credit: Pace et. al.,Physics Today (2015)
Classifying Particle Orbits In Tokamaks Is Important for Understanding Basic Physics Mechanisms Like Wave-Particle Interactions

## Slide 54
Occurs when the wave and particle orbit phases match after many cycles:
ω = lωci + pωθ + nωζ
Time to complete poloidal orbit
Time to complete cyclotron orbit
Time to complete toroidal orbit
Particle Resonance With Alfvén Eigenmode (AE) Instabilities
[W.W. Heidbrink, Phys. Plasmas 15 (2008)]
AE mode frequency
Notes: Now, fast ions can be resonant with Alfven eigenmodes if they are in phase with the mode after an integer number of orbits. There are 3 characteristic orbit frequencies, this is the ion gyromotion, then there is the time that it takes a fast ion to precess around the tokamak and complete a toroidal orbit, and then there is the time that it takes to complete a poloidal orbit. Resonance can occur if the phase of the particle and the wave match after many cycles. A nice picture to have in your head is that as the particle executes it’s orbit, it stays in phase with the same node of the mode. Power transfer can occur between the particle and the transverse component of the electric field, and in this case the energy received from the mode cause the particle to cross a topology boundary and become lost.

## Slide 55
Occurs when the wave and particle orbit phases match after many cycles:
Time to complete poloidal orbit
ω = lωci + pωθ + nωζ
Time to complete cyclotron orbit
Time to complete toroidal orbit
Particle Resonance With Alfvén Eigenmode (AE) Instabilities
[W.W. Heidbrink, Phys. Plasmas 15 (2008)]
AE mode frequency
Power transfer can occur as the ion stays in phase with the wave as it traverses the mode
[Pace, Physics Today (Oct. 2015)]
Notes: Now, fast ions can be resonant with Alfven eigenmodes if they are in phase with the mode after an integer number of orbits. There are 3 characteristic orbit frequencies, this is the ion gyromotion, then there is the time that it takes a fast ion to precess around the tokamak and complete a toroidal orbit, and then there is the time that it takes to complete a poloidal orbit. Resonance can occur if the phase of the particle and the wave match after many cycles. A nice picture to have in your head is that as the particle executes it’s orbit, it stays in phase with the same node of the mode. Power transfer can occur between the particle and the transverse component of the electric field, and in this case the energy received from the mode cause the particle to cross a topology boundary and become lost.

## Slide 56
Projection of 80 keV D+ orbit in the DIII-D tokamak
[R. B. White, Theory of toroidally confined plasmas, Imperial College Press (2001)]
The Fast Ion Distribution Function Is “Most Simply” Described Using Constants of Motion
Notes: As an introduction, fast ions are most simply described using constants of motion in what’s called orbit topology space. So this is a plot of magnetic moment, normalized by particle energy, vs the toroidal canonical angular momentum. In this space, you can classify particle orbits as, say trapped, so these are banana orbits, co-passing, so they are traveling in the same direction as plasma current, counter passing. Some special orbits exist with names like potato or stagnation.
So for example, this is the projection of a full energy fast ion orbit for a counter passing particle. If the particle had slightly higher perpendicular velocity, it would be located on the other side of the topological boundary and the particle would be lost.
Magnetic moment = mv_perp^2/(2B)

## Slide 57
Projection of 80 keV D+ orbit in the DIII-D tokamak
[R. B. White, Theory of toroidally confined plasmas, Imperial College Press (2001)]
Small Changes in Particle Energy Can Cause Large Changes in Orbit Topology
Notes: As an introduction, fast ions are most simply described using constants of motion in what’s called orbit topology space. So this is a plot of magnetic moment, normalized by particle energy, vs the toroidal canonical angular momentum. In this space, you can classify particle orbits as, say trapped, so these are banana orbits, co-passing, so they are traveling in the same direction as plasma current, counter passing. Some special orbits exist with names like potato or stagnation.
So for example, this is the projection of a full energy fast ion orbit for a counter passing particle. If the particle had slightly higher perpendicular velocity, it would be located on the other side of the topological boundary and the particle would be lost.
Magnetic moment = mv_perp^2/(2B)

## Slide 58
Example of distribution function F(E,m,Pϕ) for neutral beam injection, which is anisotropic and non-Maxwellian
neutral beam injection
[R. B. White, Theory of toroidally confined plasmas, Imperial College Press (2001)]
There Can Be Several Different Populations of Fast Ions In Fusion Devices
The distribution function for fusion products (alpha particles) is isotropic
Notes: This is an example of the types of fast ions created by neutral beam injection. You can see that neutral beam injection creates a distribution function that is anisotropic and non-Maxwellian.

## Slide 59: Active Research: Calculating the Energetic Particle Distribution Function After Transport by Instabilities
Beam Deposition
Resonance (Many Modes)
Transport can occur if fast ions intersect AE resonances in this “phase space” plot
In certain conditions, AEs can cause significant transport of fast ions and significantly degrade fusion performance  We are working on controlling/avoiding AEs
Notes: Because of this resonance phenomenon, AE transport is inherently a phase space dependent process. So back to orbit topology space diagram, the red squares represent all of the possible resonances that are possible for just a single Alfven eigenmode. You can see that AEs can affect certain parts of fast ion phase space, but leave other parts unaffected. So you would expect to measure tranpsort at the intersection where your diagnostic is sensitive, where fast ions are present, and where fast ions can resonate with AEs. In reality there are often multiple modes which end up basically painting much of fast ion phase space.

## Slide 60
Charged particles undergo gyromotion about magnetic fields, and are free to move along the magnetic field line.
Depending on magnetic field geometry or the presence of other forces like electric fields, particles can drift across field lines (and even leave the systemhit the walls).
(One) challenge for fusion energy research is to confine enough charged particles that are energetic enough for long enough lengths of time to achieve sustained fusion.
Conclusions