## Slide 1: Plasma Science: the unsung engine of the digital age
Steven Shannon
22 June 2022
Peter Clarke, “Applied Materials readies DRIE machines for MEMS, EETimes Magazine, 22 March 2012

## Slide 2
Peter Clarke, “Applied Materials readies DRIE machines for MEMS, EETimes Magazine, 22 March 2012
How do we make things so small?
Current SOA is 5nm!!!
How do we control the direction of a chemically driven process?

## Slide 4
The majority of plasma processing resides in a pretty small window in “plasma space”
108cm-3 < ne < 1012cm-3
0.5eV < Te <10eV
Less than 1% of the gas is actually ionized
The background gas (and ions) stay roughly near room temperature

## Slide 5: The basic challenge – fabrication of very complex features with dimensions ~10nm
Harmeet Singh, “Overcoming challenges in 3D NAND volume manufacturing, Solid State Technology Magazine, July 2017
Dick James, “The Second Shoe Drops – Samsung V-NAND Flash”, www.chipworks.com, 5 August 2014

## Slide 6
Why? Because the smaller the device, the faster it runs…

## Slide 7: There are lots of challenges to make this device… we will focus on High Aspect Ratio etching in dielectric materials
Peter Clarke, “Applied Materials readies DRIE machines for MEMS, EETimes Magazine, 22 March 2012

## Slide 8: The “classic” experiment that drove plasma etch
Coburn and Winters, J. Vac. Sci. Technol. 16, 391
Silicon Wafer
XeF2
Ar+

## Slide 9
The “classic” experiment that drove plasma etch
Coburn and Winters, J. Vac. Sci. Technol. 16, 391
Silicon Wafer
XeF2
Ar+
F
SiF4

## Slide 10
The “classic” experiment that drove plasma etch
Coburn and Winters, J. Vac. Sci. Technol. 16, 391
Silicon Wafer
XeF2
Ar+
F
SiF4

## Slide 11
The “classic” experiment that drove plasma etch
Silicon Wafer
XeF2
Ar+
Ar+ @500V
Si

## Slide 12
The “classic” experiment that drove plasma etch
Coburn and Winters, J. Vac. Sci. Technol. 16, 391
Silicon Wafer
XeF2
Ar+
Ar+ @500V
Si

## Slide 13
The “classic” experiment that drove plasma etch
Silicon Wafer
XeF2
Ar+
Ar+ @500V
Si
MD simulation by Graves group, UC Berkeley

## Slide 14
The “classic” experiment that drove plasma etch
Coburn and Winters, J. Vac. Sci. Technol. 16, 391
Silicon Wafer
XeF2
Ar+
F
Ar+ @500V
SiFx

## Slide 15
The “classic” experiment that drove plasma etch
Coburn and Winters, J. Vac. Sci. Technol. 16, 391
What we learned: ion bombardment and reactive chemistries work in synergy to accelerate chemical reactions on the surface and accelerate processes like etching
F
Ar+
Horizontal surfaces:
Reactant + ions = fast removal
Vertical surfaces
Reactant only
Slow removal or
passivation
Chemically impervious mask

## Slide 16
The “classic” experiment that drove plasma etch
What we learned: ion bombardment and reactive chemistries work in synergy to accelerate chemical reactions on the surface and accelerate processes like etching
F
Ar+
Horizontal surfaces:
Reactant + ions = fast removal
Vertical surfaces
Reactant only
Slow removal or
passivation
Chemically impervious mask

## Slide 17
The “classic” experiment that drove plasma etch
What we learned: ion bombardment and reactive chemistries work in synergy to accelerate chemical reactions on the surface and accelerate processes like etching
F
Ar+
Horizontal surfaces:
Reactant + ions = fast removal
Vertical surfaces
Reactant only
Slow removal or
passivation
Chemically impervious mask

## Slide 18: Fortunately this technology exists…
Applied Materials Advantage Etch System
Silicon Wafer
CF4
Ion acceleration
Through RF sheath

## Slide 19: Fortunately this technology exists…
Applied Materials Advantage Etch System
Silicon Wafer
CF4
Ion acceleration
Through RF sheath

## Slide 20: Fortunately this technology exists…
Applied Materials Advantage Etch System
Costs more than a 53 foot yacht (~ $1,000,000)
Has a vacuum chamber that can provide the same conditions as outer space (base pressure < 1mTorr)
Turbo pump that spins faster than a jet engine (~25,000 RPM)
More RF power than a college radio station (~10,000 Watts)
Registered with the Federal Communications Commission

## Slide 21: And it’s only getting bigger…

## Slide 22: Fortunately this technology exists…

## Slide 23: Seriously…. Fortunately this technology exists…
Without plasma processing we would be running on 1990’s era computing – 8MB memory, 500MB Hard Drive, no flat panels, 24 bit video, 28.8 kbs connectivity, 33MHz clock speed
Pace of innovation is ridiculous… presents real R&D challenges, especially on the basic science side…

## Slide 24: So… how does it work? We need two things…
Silicon Wafer
CF4
Ion acceleration
Through RF sheath
Electron driven “breaking” of molecules… don’t use thermal energy, use electron bombardment. This keeps the gas cool
Ion acceleration normal to the surface using naturally occurring electric fields at the plasma edge
If I can combine electron impact driven chemistry and controlled ion bombardment, I have an anisotropic reactor!
Plasmas can do both!

## Slide 25: Building a simple plasma reactor, which in its simplest form is basically a high voltage gas filled capacitor
L
p, ng, Tg
R
Will try to keep this as simple as possible, but unfortunately at some point things have to get a little ugly, but not super ugly…

## Slide 26: What happens if we fill this capacitor with a plasma?
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, p, ng, Tg
typically

## Slide 27
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, p, ng, Tg
typically
At time t = 0, the entire cylinder is filled with an equal distribution of electrons and ions
What happens if we fill this capacitor with a plasma?

## Slide 28
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, p, ng, Tg
typically
At time 0 < t < de/ve, charged species move to the wall, where they are lost to the system as the charge goes to ground or accumulates on surface
-+-+-+-+-+-+-+-+-
e-
i+
e-
i+
What happens if we fill this capacitor with a plasma?

## Slide 29
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, p, ng, Tg
typically
de is the Debye Length of the plasma – the distance needed for a plasma to locally screen out a point charge, and is a typical “scale length” for a plasma
-+-+-+-+-+-+-+-+-
e-
i+
e-
i+
What happens if we fill this capacitor with a plasma?

## Slide 30
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, p, ng, Tg
typically
At time de/ve < t < de/vi, Since electrons are thousands of times lighter than ions, they are more mobile and an electron depletion region forms around the surfaces
---+---+---+---+---
i+
e-
e-
i+
d = L – 2s
s
s
What happens if we fill this capacitor with a plasma?

## Slide 31
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, p, ng, Tg
typically
At time t > de/vi the electron depletion creates an electric field to zero diffusion current similar to the depletion region of a PN junction
---+---+---+---+---
i+
e-
e-
i+
d = L – 2s
s
s
E
E
What happens if we fill this capacitor with a plasma?

## Slide 32
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
---+---+---+---+---
i+
e-
e-
i+
d = L – 2s
s
s
E
E
in 5eV Ar
5eV Ar 1010cm-3
Vf
What happens if we fill this capacitor with a plasma?

## Slide 33
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
---+---+---+---+---
i+
e-
e-
i+
d = L – 2s
s
s
E
E
Vf
What happens if we fill this capacitor with a plasma?
The electric field accelerates ions normal to the surface, providing ion flux to ONLY horizontal surfaces and accelerating reactions on those surfaces
ACHIEVED!

## Slide 34
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
Meanwhile, in the bulk plasma region, the faster electrons collide mainly with neutral gas species
Elastic collisions (polarization scattering)
Inelastic collisions – excitation, dissociation
Ionization collisions – have a threshold energy, produce more e-i pairs
What happens if we fill this capacitor with a plasma?

## Slide 35
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
Meanwhile, in the bulk plasma region, the faster electrons collide mainly with neutral gas species
Elastic collisions (polarization scattering)
Inelastic collisions – excitation, dissociation
Ionization collisions – have a threshold energy, produce more e-i pairs
What happens if we fill this capacitor with a plasma?
e
E > 5eV
C-F bond energy
~5eV

## Slide 36
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
Meanwhile, in the bulk plasma region, the faster electrons collide mainly with neutral gas species
Elastic collisions (polarization scattering)
Inelastic collisions – excitation, dissociation
Ionization collisions – have a threshold energy, produce more e-i pairs
What happens if we fill this capacitor with a plasma?
e
E < 5eV

## Slide 37
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
The rate per unit volume of a specific collision is determined by four factors:
The number of electrons ne
The number of targets for the electron to hit ntarget
The velocity of the electron (2Ee/me)1/2
The effective size of the target atom or molecule for that collision, the cross section s
What happens if we fill this capacitor with a plasma?
e
E < 5eV

## Slide 38
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p, ng, Tg
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
The velocity of the electron – be careful here, electrons in a plasma have a distribution of energies, not always Maxwellian
30 mTorr
300 mTorr
J. Appl. Phys. 73 (8), 1993 3657-3664
What happens if we fill this capacitor with a plasma?
e
E < 5eV

## Slide 39
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
ni, Ti, ne, Te, Vp, p,
Eiz, Eex, ng, Tg
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
The target size of the atom or molecule can be a strong function of an individual electron’s energy
Elastic
Excitation (composite)
Ionization
www.lxcat.net/SIGLO
Eiz, Eex
What happens if we fill this capacitor with a plasma?
e
E < 5eV

## Slide 40
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
Assume a form of fe(E)
K
www.lxcat.net/SIGLO
BOLSIG solver, Maxwellian Assumption
ni, Ti, ne, Te, Vp, p, Kme,
Kex, Kiz, Eiz, Eex, ng, Tg
What happens if we fill this capacitor with a plasma?
e
E < 5eV

## Slide 41
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
Assume a form of fe(E)
K
www.lxcat.net/SIGLO
BOLSIG solver, Maxwellian Assumption
ni, Ti, ne, Te, Vp, p, Kme,
Kex, Kiz, Eiz, Eex, ng, Tg
What happens if we fill this capacitor with a plasma?
This gives us reaction rates (K), just like in chemistry, but they are a function of the electron’s temperature, NOT the gas temperature
But – we do get reactive gas species without heating up the background gas much

## Slide 42
Note: most processing “plasmas” are still composed of around 99.9% neutral gas species
typically
R
L
typically
n
e-
d = L – 2s
Vf
n
n
n
n
i+
Assume a form of fe(E)
K
www.lxcat.net/SIGLO
BOLSIG solver, Maxwellian Assumption
ni, Ti, ne, Te, Vp, p, Kme,
Kex, Kiz, Eiz, Eex, ng, Tg
What happens if we fill this capacitor with a plasma?
This gives us reaction rates (K), just like in chemistry, but they are a function of the electron’s temperature, NOT the gas temperature
But – we do get reactive gas species without heating up the background gas much and we can control it with electron temperature
ACHIEVED!

## Slide 43: However - the list of reactions gets very long, and very difficult to set up and solve balance equations
Imagine the list of pertinent reactions for something like SF6, CF4, C4F8, or Si(OC2H5)4 (TEOS)
Even worse, realize that rarely is only one gas used for a process. Dielectric etch would run Ar, O2, and C4F8 at the same time.
And even if you could build a complete set of reactions, the cross sections and rate constants for many of these species are at best “qualitative”

## Slide 44
And the list of reactions gets very long, and very difficult to set up and solve balance equations
624 Reactions!

## Slide 45
624 Reactions!
Electron Impact Driven
Charge Exchange Free Electron Forming
Positive (and negative)
Ion Driven Reactions
Excited Atomic and
Molecular Specie Driven
“Boring” Gas Phase Ground State Stuff
Boltzmann
Reactions
Reactions where we have to “guess”
And the list of reactions gets very long, and very difficult to set up and solve balance equations

## Slide 46: Plasma technology has had (and still does) need to keep pace
1990’s – etch rate, etch selectivity, dual damescene
2000’s – profile shape, aspect ratio, 300mm
2010’s – aspect ratio, complex material stacks, residual material damage
2020’s – (one person’s opinion at least) – new pathways for anisotropy + advanced chemistry control to maintain anisotropy with minimal device damage down to the atomic scale
Keren Kanarik et. al., “Moving atomic layer etch
from lab to fab”, Solid State Technology Magazine,
January 2014
Silicon Quantum Dot
Single electron transistor
Michael Wang, Lithography,
Intech Press (2010)
Kevin Gibb, “Samsung’s 14 nm LPE
FinFET Transistors”, EETimes, 2016

## Slide 47: Summary – we need two things to drive device fabrication – ions and reactive low temperature chemistry. Plasmas give us both.
Silicon Wafer
CF4
Ion acceleration
Through RF sheath
Electron driven “breaking” of molecules… don’t use thermal energy, use electron bombardment. This keeps the gas cool
Ion acceleration normal to the surface using naturally occurring electric fields at the plasma edge

## Slide 48: Summary – using plasma technology allows us to combine Thing 1 + Thing 2 to produce the nano-scale devices in electronic equipment today
Electron driven “breaking” of molecules… don’t use thermal energy, use electron bombardment. This keeps the gas cool
Ion acceleration normal to the surface using naturally occurring electric fields at the plasma edge

## Slide 49: Acknowledgements
Countless students, engineers, scientists, and collaborators over the last 25+ years