## Slide 1: Lane B. Carasik, Ph.D. – Happy Pride Month!
Fluids in Advanced Systems and Technology (FAST) Research Group, Virginia Commonwealth University
Email: lbcarasik@vcu.edu – Group Website: fastresearchgroup.weebly.com
Heat Removal for First Wall Components, Blankets, and Power Conversion
Notes: Name
Year
School
FAST
Title

## Slide 2: How’d I get here?
Middle Georgia College
Associates in Math
B.S. in Nuclear Engineering
Undergrad research in experimental thermal hydraulics
Ph.D. in Nuclear Engineering
Coursework in Aero, Mech, and Civil
ATL - Getty Images
knoxnews
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 3: How’d I get here?
Summer REU (NSF CREATE)
Undergrad Research
Summer Intern
Summer Intern
Visiting Researcher
Grad Intern
Grad Intern
CFD Engineer
Nuclear Thermal Fluids Engineer
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 4: What am I doing in the Fusion Community?
FS&T Associate Editor (2022-Present)
ITER Workshop Participant and Report Writing Support (2022)
Liquid Immersion Fusion Blanket Senior Design Team!
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 5: Outline
First Wall Components within Fusion Devices
System Level Viewpoint
Power Conversion Thermodynamic Cycles
Component Level Heat Removal Mechanisms
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 6: First Wall Components within Fusion Devices
1ITER Organization, 2021, https://www.iter.org/
ITER1
ITER Plasma Facing Component1
Divertor (Up to 20 MW/m2)
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 7: First Wall Components within Fusion Devices
1ITER Organization, 2021, https://www.iter.org/
ITER1
ITER Blanket1
(~4.5 MW/m2)
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 8: Dual Cooled Lead Lithium Concept
1S. Smolentsev, Fluids 2021, 6(3), 110; https://doi.org/10.3390/fluids6030110
Schematic of the DCLL with PbLi and Helium 1st wall cooling1
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 9: Liquid Immersion Blanket Concept (ARC)
1S. Ferry, 2023, https://suli.pppl.gov/2023/course/SULI%202023%20presentation.pdf
ARC Overview1
2https://news.mit.edu/2018/nas-report-right-path-fusion-energy-1221
Notes: Twisted tubes cause more mixing of the fluid
Cause greater turbulence
More turbulence = better heat transfer
Better heat transfer = more efficient = more power more money/less fuel/less coolant cause salts $$
Specifically were interested in the flow around the outside of the tubes

## Slide 10: Why Heat Removal? (System Level)
Cooling of components to prevent degradation and damage
Why use fusion devices at all?
  Power generation
Power Generation Schematic for a Fusion Device - MIT Plasma Science and Fusion Center (PSFC)1
1https://news.mit.edu/2018/nas-report-right-path-fusion-energy-1221
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 11: System Level – Power Cycles
Based on a Rankine power cycle that is built upon centuries of experience in the power industry
Power Generation Schematic for a Fusion Device - MIT Plasma Science and Fusion Center (PSFC)1
1https://news.mit.edu/2018/nas-report-right-path-fusion-energy-1221
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 12: System Level – Power Cycles
Regardless of heat source, most power generation results in the same thing, boiling water to spin a turbine that causes a generator to create electricity.
Power Generation Schematic for a Fusion Device - MIT Plasma Science and Fusion Center (PSFC)1
1https://news.mit.edu/2018/nas-report-right-path-fusion-energy-1221
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 13: System Level – Power Cycles
There are two common forms of power cycles that could be used:
  Rankine (Liquid - water based)
  Brayton (Gas – helium or others based)
1https://energyeducation.ca/encyclopedia/Rankine_cycle
2https://energyeducation.ca/encyclopedia/Brayton_cycle
Brayton Cycle
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 14: System Level – Power Cycles
Both cycles can be made more complex with reheating, regeneration, multiple stages, to maximize the amount of useful energy out vs. heat in
In this case, the TH or TC are the hottest and coldest reservoir temperatures.
1https://energyeducation.ca/encyclopedia/Rankine_cycle
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 15: System Level – Power Cycles
Both cycles can be made more complex with reheating, regeneration, multiple stages, to maximize the amount of useful energy out vs. heat in
We have a few options, lower our final heat sink temperature, raise our operating temperature, but never can reach ideal efficiencies.
1https://energyeducation.ca/encyclopedia/Rankine_cycle
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 16: System Level – Heat Removal
A critical aspect of heat removal is ensuring we understand the heat transfer mechanisms that control our power cycle capabilities, material temperature limits, and instrumentation/control schemes.
1ITER Organization, 2021, https://www.iter.org/
ITER Blanket1
(~4.5 MW/m2)
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 17: Heat Transfer Mechanisms
Heat Transfer occurs whenever there is a temperature difference between two objects
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 18: Heat Transfer Mechanisms
Heat Transfer occurs in:
  Solids – Gases – Fluids – Plasmas - Others?
  As a continuum (not individual particles)
Very General Conservation of Energy Equation
Enthalpy Formulation
Temperature Formulation
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 19: Heat Transfer Mechanisms
Heat Conduction (Conductive Heat Transfer)+
  Can occur within an object and between objects in contact
  Described using diffusion operator () in the energy equation
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 20: Heat Transfer Mechanisms
Heat Convection (Convective Heat Transfer)
  Involves a fluid (liquid or gas) that is moving due to mechanical or buoyant forces
  Described using the advective operator ( or )
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 21: Heat Transfer Mechanisms
Heat Convection (Convective Heat Transfer)
  Two forms (Free/Natural and Forced Convection)
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 22: Heat Transfer Mechanisms
Heat Convection (Convective Heat Transfer)
  Two forms (Free/Natural and Forced Convection)
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 23: Heat Transfer Mechanisms
Heat Radiation (Irradiative Heat Transfer)
Notes: Simulated and modeled using Nek5000
Open source, CFD code
Mix of Fortran77 and C, uses SEM to solve the unsteady NS eqns
Capable of different modeling techniques such as DNS, and LES/RANS for turbulence modeling
Nek5000 is primarily used for CFD modeling in the nuclear industry and has been extensively verified and validated

## Slide 24: Scaling and Similitude for Fusion Device Design
We take advantage of surrogate fluids for molten salts, liquid metals, and gases to do scaled heat transfer and fluid dynamics experiments.
Relevant scaling parameters/non-dimensional numbers:
Desired Heat Transfer/Fluid Dynamics Design Information:
Cabral, A., et al., “Identification of Surrogate Fluids for Molten Salt Coolants used in Energy Systems Applications including Concentrated Solar and Nuclear Power Plants,” Int. J. Energy Res., Vol. 46(3), pp. 3554-3571, 2022

## Slide 25: Similitude of Heat Transfer
Fluorides:
Chlorides:
Nitrates:
Cabral, A., et al., “Identification of Surrogate Fluids for Molten Salt Coolants used in Energy Systems Applications including Concentrated Solar and Nuclear Power Plants,” Int. J. Energy Res., Vol. 46(3), pp. 3554-3571, 2022

## Slide 26
Different forms of heat transfer enhancements exists:
Swirl flow inserts
Internal fins
Rifling/grooves
Others
Performance quantified by the
Thermal Performance Factor
Types of Heat Transfer Enhancements

## Slide 27: Computational Fluid Dynamics
Tutwiler, S., Shaver, D., Carasik, L. B., “Determination of Aspect Ratio Influence on Flow and Heat Transfer Behavior in Twisted Elliptical Tubes for Molten Salt Applications,” Adv. In Thermal Hydraulics, 2022
Data Reduction (Triangles are Simulations)

## Slide 28: Experimental Fluid Dynamics
Wiggins, C., et al., “Noninvasive interrogation of local flow phenomena in twisted tape swirled flow via positron emission particle tracking (PEPT),” Nuc. Eng. Des., Vol. 387, pp. 1116012022, 2022.
Particle tracking within pebble bed fusion device geometries

## Slide 29: Acknowledgements
Thanks to Dr. Arturo Dominguez, PFURO, DOE FES, US DOE Office of Science, and more for this opportunity!

## Slide 30: Thank you!

## Slide 31: Additional Resources
Heat Transfer Lectures:
https://www.youtube.com/playlist?list=PLZOZfX_TaWAHZOgn8CRjpqRElp5Dd-GaY
Fluid Mechanics Lectures:
https://www.youtube.com/watch?v=clVwKynHpB0&list=PLZOZfX_TaWAGocs2k5QmTL44OKOl7rn34&ab_channel=CPPMechEngTutorials
https://www.youtube.com/watch?v=PXjZ7xEAqsU&list=PLZOZfX_TaWAH0baRhA8OosWVbEsJK5sPe&ab_channel=CPPMechEngTutorials
https://www.youtube.com/watch?v=kxhTMc8tyEo&list=PLZOZfX_TaWAE7uM59dIBr-rH73WTJCcp_&ab_channel=CPPMechEngTutorials