## Slide 1
Objectives and status of the ITER Project
Alberto Loarte
Science Division
Science, Controls, and Operation Department
ITER Organization
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization

## Slide 2
Outline of talk
Personal Journey
ITER Mission, Basis, Goals, Scenarios and Overall Design
ITER Project and Overview of Construction Status
ITER Research Plan (IRP) and burning plasma physics
Conclusions

## Slide 3
Personal Journey
Bachelor in Theoretical Physics (interested in Astrophysics) at UCM – Madrid
PhD in fusion plasma theory at UCM  short stay at JET (2  6 months)
Change of PhD topic : edge plasma experiments and modelling at JET
Postdoc at JET 2-D edge modelling and experiment (detachment)  participation in ITER expert groups (International Tokamak Physics Activities)
Move to ITER EU Home Team (IPP-Garching)  R&D for ITER (exp. + modelling - ELMs R&D), EU R&D PWI programme management, ITPA DivSOL
Move to ITER Organization  Science, Controls and Operation Department
  Edge/Pedestal physics and Edge-core plasma integration, Science and Technology Advisory Committee Secretary, ITPA Edge and Pedestal
  Section Leader Confinement & Modelling, STAC Secretary, ITPA Transport & Conf.
  Science Division Head :
    ITER Research Plan, Plasma Control System design, Integrated Modeling and Analysis Suite

## Slide 4
ITER Mission, Basis, Goals and overall design

## Slide 5
ITER Mission
To demonstrate the scientific and technological feasibility of fusion power as energy source for humankind
R=6.2 m, a=2.0 m
  D (2H) + T(3H) fusion

## Slide 6
ITER
  Net production of fusion energy
  Pfusion (4He + n) = Pa+Pn > Pexternal-heat
  Q = Pfusion (4He + n)/Pexternal-heat
  Ptotal-heat = Pa (4He) + Pexternal-heat
  Pa/Pexternal-heat = Q/5
  To achieve high Q (> 5) requires hot (> 10 keV) plasmas with sufficient density that keep energy for sufficiently long time
  nitETi > 31021 m-3 s keV
ITER Basis: DT Fusion Power Production

## Slide 7: ITER Basis: Magnetic Confinement
At high temperatures required for fusion D and T are ionized (“Plasma”)  hot DT can be contained by magnetic fields
Magnetic fields are used to :
Reduce thermal losses across magnetic field
Provide stabilizing compression force to compensate hot plasma expansion
Tokamak
Notes: utile = “relevant” ?
Pertinente? Réalisable?

## Slide 8: ITER Basis: Plasma Heating
To achieve fusion power production T ~ 10 keV  Heating of Plasma is required :
Ohmic heating = Ip2 Rp; Rp ~ T-3/2  insufficient
Radio Frequency Heating
Injection of energetic atoms
Notes: utile = “relevant” ?
Pertinente? Réalisable?

## Slide 9
th  IpR2P-2/3
Energy confinement difficult to predict quantitatively  use scalings from experiments + plasma physics limits to dimension ITER to achieve its goals
ITER Basis: Energy Confinement (tE)
Plasma Current
Major Radius
Input Power
a
b
R

## Slide 10
ITER Goals
  Pulsed operation:
  Q ≥ 10 for burn lengths of 300-500 s inductively driven current
   Baseline scenario 15 MA / 5.3 T
  Pa ≥ 2 Pexternal-heat
  Long pulse operation:
  Q ~ 5 for long pulses up to 1000 s
   Hybrid scenario ~ 12.5 MA / 5.3 T
  Steady-state operation:
  Q ~ 5 for long pulses up to 3000 s, with fully non-inductive current drive
   Steady-state scenario ~ 10 MA / 5.3 T
R=6.2 m, a=2.0 m

## Slide 11
ITER Q = 10 scenario (300 – 500 s burn)
Based on conventional sawtoothing H-mode with H98 = 1  scenario used for the design of magnets and components (15 MA/5.3 T)
Paux = PNBI + PECH (+ PICH) ~ 50 MW  Alpha-heating dominant scenario with non-inductively driven current ~ 35%

## Slide 12
Few key ingredients to achieve ITER’s fusion goals - I
Achievement of high energy confinement plasmas
  Low confinement (L-mode): pulsed operation ()
  High confinement (H-mode): pulsed operation ()
/ 1.5
High confinement
  Improved high confinement: long pulse () / steady-state ()
Improved high confinement
Low
confinement
Power threshold for transition from L to H-mode:
(empirical basis)
Pfusion ~ Wplasma-th2
Plasma Pressure (a.u.)

## Slide 13
Edge-core integration : stationary and ELM transient power fluxes
R. Pitts PSI 2018
qdiv < 10 MWm-2
ELM control : Mitigation by fELM increase and suppression
Radiative Dissipation
JOREK
G. Huijsmans
Few key ingredients to achieve ITER’s fusion goals - II

## Slide 14
MHD stable plasma operation + mitigation if global instabilities develop (disruptions)
Few key ingredients to achieve ITER’s fusion goals - III
Large thermal and electromagnetic loads
Wplasma-th
Wplasma-mag
Jhalo + Jeddy x B forces
M. Lehnen EPS 2017
Wplasma-mag

## Slide 15
ITER Main Design Features

## Slide 16
ITER Heating and Current Drive systems

## Slide 17
ITER Diagnostics and 3-D coils (Error Field, ELM control)
Diagnostics: ~ 60 instruments measuring ~ 100 parameters
External error field correction coils + internal ELM control coils

## Slide 18
ITER Disruption Mitigation System
JET

## Slide 19
Tritium Breeding : Test Blanket Systems
Tritium not available in sufficient amounts for large scale nuclear fusion energy production  Tritium needs to be produced in-situ (n + Li)
T production schemes will de demonstrated in ITER (at small scale)
Different test blanket systems will be installed in ITER to test different combinations of design options:
Liquid metal breeder
Solid breeder
Helium coolant
Water coolant

## Slide 20
ITER as a Project and overview of Construction Status

## Slide 21
ITER
The seven ITER Members represent more than 50% of the world’s population and about 85% of the global GDP
China EU India Japan Korea Russia USA
28 June 2005: The ITER Members unanimously agreed to build ITER on the site proposed by Europe
21 November 2006: The ITER Agreement is signed at the Élysée Palace, in Paris.
Global challenge, global response
Notes: KD: “represent” KD: Remove “on” from dates

## Slide 22
Construction ITER – Who manufactures What ?
Notes: THE objectives set out for ITER are basically two:
ONE: to obtain and study a plasma where the alfa particle heating is dominating all other forms of heating.
ITER will operate with a value of capital Q greater than 10.
The fusion power in ITER will be about 500MW, the input power about 50MW.
And TWO: it has to integrate the technology required for future use of fusion as an energy source

## Slide 23
ITER Cryostat
Largest stainless steel high-vacuum pressure container ever built
Provides high-vacuum and ultra-cool environment
Height: 30 m
Diameter: 30 m
Weight: 3,850 t

## Slide 24
Double wall steel container
blanket modules
cooling water
High-vacuum environment
Primary containment barrier
Volume: 1,400 m3
Plasma volume: 840 m3
Weight: 8,500 t
ITER Vacuum Vessel

## Slide 25
ITER Magnet System
Central solenoid
13 m high
1,000 tons
18 toroidal field coils
17 m high
360 tons each
6 poloidal field coils
8-24 m in diameter
200-400 tons

## Slide 26
Itinerary of ITER Components
= Itinerary of ITER Components
ITER Site
Notes: 26

## Slide 27
Many massive arrivals in 2020-23 (few shown)
TF
TF
PF6
Vacuum Vessel Sector # 6
First Central Solenoid Module
PF1

## Slide 28
ITER Site Construction Status

## Slide 29
March 2023
ITER construction site drone view

## Slide 30
Worksite progress
Cryostat upper cylinder
(temporary storage)
RTE (France) 400 kV switchyard
Tokamak Complex
Cryoplant
Cryoplant
Radiofrequency Bdg.
Cryostat workshop

## Slide 31
ITER Control Room

## Slide 32
Balance of plant
Towards commissioning
Cryoplant:
5 000 tonnes of equipment
LHe: 25 t Cooling Power: 75 kW at 4.5 K (Helium) 1300kW at 80 K (Nitrogen)

## Slide 33
ITER Tokamak Assembly Status

## Slide 34
Assembly Hall and Tokamak building
Tokamak components assembled in assembly hall and lifted by cranes into tokamak pit

## Slide 35
On May 26-27 2020, the base of the Cryostat (1,250 t; procured by India) was successfully inserted into the Tokamak Assembly Pit.
A crucial milestone
28 July 2020: remote celebration by 7 ITER Members Heads of State and French President

## Slide 36
Sub-sector assembly
Assembly of Vacuum Vessel, Thermal Shield and 2 Toroidal Field coils
TF Coil Assembly
Finalized Sector Assembly before transfer to pit

## Slide 37
VV Sector 7 with TF coil 9 on right arm of SSAT-1

## Slide 38
11 May 2022
Sector 6 fully lifted out of SSAT-2 and rotated 90

## Slide 39
11 May 2022
Over the tokamak pit wall: 20 cm gap

## Slide 40
11 May 2022
Lowering into the tokamak pit

## Slide 41
14 June 2022
In-place and alignment procedure started

## Slide 42
Alignment procedure completed
15 October 2022

## Slide 43
Alignment procedure guided by physics assessment of error fields
TFC error field analysis will be extended to other coils and components
Alignment targets ensure that for 99% of the cases TF assembly will contribute less than 33% of the n = 1 overlap field (ITPA scaling)
(15 MA/5.3T : plasma 1 SOF, plasma 2 EOB)

## Slide 44
September 2022
VV Sector 8 in vertical position in the upending tool ready for transfer to SSAT-2
VV Sector 7 assembly nearly complete

## Slide 45
First module of the 1000 tonne, 18 m tall central solenoid positioned (to ±1 mm accuracy in plane) on the bespoke assembly platform. Second module awaiting on the right.
June 2023

## Slide 46
Issues found and solutions
more details in
https://www.iter.org/newsline/-/3818
and
https://www.iter.org/newsline/-/3830

## Slide 47
Corrosion of cooling pipes in thermal shields

## Slide 48
Dimensional non-conformities of VV sectors impacting sector-to-
sector welding

## Slide 49
Solution for VV thermal shield  remove old pipes and re-weld new pipes (different steel and welding process/material) + re-manufacture of few panels  requires removal of installed shields from sectors
Solution for Cryostat thermal shield  leave old pipes (unused) and re-weld new pipes (different steel/welding process/material) on-site
Solution to VV non-conformity  remove and add material to meet required dimensions (73 - 400 kg per octant)
Repairs to about to start (contracts will be signed soon)  duration of repairs cannot be precisely estimated at this time

## Slide 50
ITER Research Plan (IRP) and burning plasma physics

## Slide 51
ITER Research Plan (IRP)
IRP describes strategy for R&D to achieve Project goals starting from First Plasma to Q = 10 (300-500 s),Q = 5 (1000 s) & Q = 5 steady-state
Proposed R&D is supported by available systems in each phase
Initial phase H/He (and D) to demonstrate :
  15 MA/5.3 T plasmas in L-mode
  Low/Medium current plasmas (Ip = 5 – 7.5 MA) in H-mode
Main phase (D and DT) to demonstrate :
  Burning Q = 10 plasmas
  Long Pulse Q = 5 plasmas
Details under reconsideration

## Slide 52
Fusion Power Operation (D/DT)
Main elements of experimental programme:
  Recommission systems with D plasmas (H&CD, diagnostics)
  Demonstration of D H-mode integrated operation at 7.5 MA/2.65 T and expansion towards higher Ip/Bt
  Introduction of T in trace levels up to ~ 50% D/ 50% T
  Increase of Ip/Bt towards 15 MA/5.3T  optimization of Q and extension of burn length
  Development of long pulse scenarios at Ip < 15 MA
  Demonstration of Q ≥ 10 goal
  Optimization of Q in long pulses (1000 s) and demonstration of Q ~ 5 goal
  Optimization of Q in steady-state pulses (3000 s) and demonstration of Q ~ 5 goal

## Slide 53
ITER burning plasma scenarios

## Slide 54
ITER Q = 10 scenario (300 – 500 s burn)
Based on conventional sawtoothing H-mode with H98 = 1  scenario used for the design of magnets and components (15 MA/5.3 T)
Paux = PNBI + PECH (+ PICH) ~ 50 MW  Alpha-heating dominant scenario with non-inductively driven current ~ 35%

## Slide 55
ITER Q ≥ 5 scenario (1000s burn)
Main option is based on improved H-mode/hybrid scenario with q(0) > 1 and H98 > 1.2 with burn length limited by q(0) reaching 1 (12.5 MA/5.3 T)
Obtained with Paux = PNBI + PECH (+ PICH) ≥ 50 MW with non-inductively driven current ~ 55%
Kim NF 2016

## Slide 56
ITER Q ~ 5 scenario (steady-state)
Based on improved H-mode/hybrid scenario with stationary q profile (q > 1) and H98 > 1.5 length limited to 3000s by hardware design (10 MA/5.3 T)
Obtained with Paux = PNBI + PECH ≥ 70 MW with non-inductively driven current ~ 100%
Kim NF 2021

## Slide 57
Q = 5 steady steady-state plasma at 10 MA
Conditions identified by 1.5-D ASTRA modelling
  EPED1+SOLPS used for pedestal and boundary
  Q=5.02, fGW=0.69
  H98=1.52, 𝛽N=3.02
  qmin=1.23
  Relatively high li(3)~0.87 mainly due to 50 MW NBI (+ 20-30 MW ECH)
  Improved confinement is essential
Polevoi – NF 2020

## Slide 58
Access to high Q conditions
Access to high Q requires build-up of Palpha since Paux is moderate and PL-H is high
Key to high Q access is density control (gas fuelling for nsep and pellet fuelling for ncore)
5MA
F. Koechl - ITER – JINTRAC - NF 2020

## Slide 59
Exit from high Q conditions
5MA
F. Koechl - ITER – JINTRAC - NF 2020
Main issue in exit from high Q is to avoid fast H-L transitions  radial plasma movement difficult to control and large power fluxes to divertor
Adjustment of Paux, fuelling and Ne seeding required to lengthen Wplasma decrease phase and avoid too high qdiv or too deep detachment

## Slide 60: Energetic ions in ITER scenarios - I
Energetic ions impact on ITER burning plasmas
  Can drive MHD Alfvén eigenmodes  energetic ion loss Pa 
  Can reduce anomalous transport level  higher tE  Pa 
  Can increase core plasma b and thus shafranov shift  increased edge stability/pressure  increased tE  Pa 
  Alfvén eigenmodes can reduce plasma turbulence  higher tE but energetic ion loss  Pa ? 
Coupling between all effects difficult to predict in quantitative way for ITER burning plasmas since Pa is dominant

## Slide 61: Energetic ions in ITER scenarios - II
Consequences of EP-driven Alfvén eigenmodes range from
  Benign saturation  significant high-amplitude bursting and transport
Extrapolation from present machines difficult due to small
Radial localisation of TAE gaps in ITER Q = 10 plasmas
Besides loss of heating, ITER first wall loads acceptable for fast ion losses of a few %
Max power transfer from a’s occurs when drift orbit width ~ mode width  n ~ 30
Many overlapping AE
ITER will quantify impact of fast ion instabilities in Q = 10 plasmas and explore means for mitigation and control

## Slide 62
Conclusions
ITER will demonstrate the scientific and technological feasibility of fusion power as energy source for humankind
ITER construction is progressing despite challenges  commitment from ITER Organization and its Members
ITER Research Plan provides experimental strategy to progress from First Plasma through to achievement of Project’s goals: Q = 10 (300-500 s), Q = 5 (1000 s) & Q = 5 steady-state
ITER high Q scenarios will address key burning plasma issues for reactors:
Coupling of physics processes in self-heated plasmas
Integration of core-edge physics to achieve burning plasma conditions with acceptable edge plasma conditions
Effectiveness of actuators and control schemes for burning plasmas  high Q disruption-free operation
In addition many fusion reactor technologies will be demonstrated (Tritium cycle, TBMs, H&CD, PFCs, etc.)

## Slide 63
Thanks for your attention