## Slide 1: The Z-challenge, radiation & diagnostics
Luis F. Delgado-Aparicio (PPPL)
06/15/2023
Princeton University
PPPL

## Slide 2: Outline
Magnetically confined fusion (MCF) plasmas and the Z-challenge
Radiation losses and the basic need of spectroscopy
Take home message: radiated power and x-ray diagnostics
Summary

## Slide 3: Class-Homework #1 …on the “fly”
After a good "couple-dozen” lectures in plasma physics and fusion, what do you think are the most important plasma quantities you need to diagnose in your experiments? Remember, diagnostics are "the key” to your access inside the plasma !!!
Challenge: Pick your top 10 (ONLY 10)
Time: Three minutes
Note: Responses cannot be changed after submitted
https://forms.gle/W6cmsJsyrpWvwRf16

## Slide 4: Tokamaks (and stellarators) spread around the world study different plasma parameters and shapes

## Slide 5: ITER will be the first time we have net energy (more energy OUT than IN)
ITER is a collaboration between USA, EU, China, Japan, Korea, India and Russia
It’s expected to produce 500MW of power using 50MW to run …this is the 1st time in history where Pout>Pin
First plasmas “expected” by 2025
Many challenges ahead!
The Z-challenge?
(low-Z vs high-Z)

## Slide 6: With the help of detailed simulations ITER scientists decided on a wall covered with low- and high-Z PFCs
Be
W
Simulations of plasma flows and plasma-wall interaction have had a decisive influence on the design of ITER wall
⇒ It’s a decision on the edge conditions which will alter core performance
Edge localized modes (ELMs) and disruptions can impact integrity of divertor cassettes

## Slide 7: The low-Z (Li, Be, C, B) vs high-Z (Fe, Mo, W) plasma facing component (PFC) challenge
Both low- & high-Z materials are currently being used as plasma facing components (PFCs), but each has technological hurdles.
Low-Z materials:
Typically have higher erosion rates
Their injection into the main chamber will result in an increase of Zeff and collisionality (ne,Z).
H-, D- & T-retention is a difficult issue! Physics or politics? Both?
Augment of Zeff will lead to:
Reduce fuel purity (nD/ne) and reactivity (Sn∝nD2 or nDnT).
But contributing less to radiated power density:
Prad = nenDLD+nenCLc+SnenZLZ
MAST, CCFE,
Oxfordshire, UK
NSTX-U @ PPPL,
Princeton, NJ
Li, B
& C

## Slide 8: The low-Z (Li, Be, C, B) vs high-Z (Fe, Mo, W) plasma facing component (PFC) challenge
Tore Supra/WEST in France
W
C
Mo
C
W
EAST in China
Mo
C-Mod @ MIT, USA
High-Z materials have good properties as a PFCs:
Low H/D/T retention.
High-heat tolerance (e.g. high melting points)
Low erosion (sputtering) rates.
Small contribution to Zeff:
Zeff ≈ nD/ne+36nC/ne+S(nZ/ne)Z2
However, if high-Z impurities accumulate to any substantial level (e.g. high-nZ/ne), this will lead to:
Exponentially enhance the radiation power losses (∝Z4): Prad=nenDLD+nenCLc+SnenZLZ
Reduce the heating efficiency and modifying the overall power balance and possibly even a radiative collapse

## Slide 9: The low-Z (Li, Be, C, B) vs high-Z (Fe, Mo, W) plasma facing component (PFC) challenge
High-Z materials have good properties as a PFCs:
Low H/D/T retention.
High-heat tolerance (e.g. high melting points)
Low erosion (sputtering) rates.
Small contribution to Zeff: Zeff=nD/ne+36nC/ne+S(nZ/ne)Z2
However, if high-Z impurities accumulate to any substantial level (e.g. high-nZ/ne), this will lead to:
Exponentially enhance the radiation power losses (∝Z4): Prad=nenDLD+nenCLc+SnenZLZ
Reduce the heating efficiency and modifying the overall power balance and possibly even a radiative collapse

## Slide 10: Target of opportunity: diagnose radiation from thermonuclear plasmas
A significant fraction of the ITER input power (50 MW) will be radiated away
Nearly 90% of the radiated power in ITER will be in the x-ray range (VITER~840 m3)
UV: 10eV < Ephoton< 200 eV
SXR: 200 eV< Ephoton< 20 keV
HXR: 20 keV < Ephoton< 400 keV

## Slide 11: Class-Homework #2: Nature…on the “fly”
3) Can you estimate the mean wavelengths l (…or type of light) emitted by cold, war, hot and burning plasmas (HINT: assume the photon energy emitted by the plasma scales roughly with its thermal energy… Ephoton=hn~Te, with h=Plank’s constant and n=c/l with c=3×108 m/s; or maybe lphoton [Å]~12398/Ephoton [eV])?:
Cold plasma: Te=2 eV
Warm plasma: Te=200 eV
Hot plasma: Te=2000 eV
Burning plasma: Te=20000 eV
700
nm
400
nm
UV
SXR
HXR
g

## Slide 12: Why is important to measure radiation emitted from tokamak and stellarator fusion-grade plasmas ?
Free info: A significant fraction of the power delivered to the plasma is lost in the form of radiation [even in an ideal pure H plasma].
In real conditions could be as high as 90%.
X-rays are the most dominant source of radiation from hot plasmas: hn~Te:
Exercise: For 100 eV<Te<20 keV ⇒ 0.5<l<130 Å ⇒ X-rays!
Measurement of power losses in the x-ray range enable the characterization of parameters such as, ne, nZ, Te, Ti, vf, vq, to be used in describing/studying:
  MHD and reconection events (from hot core to cold edge).
  Transport coefficients (e.g. diffusivity and pinch velocity).
  Radial electric field (Er)
  Magnetic flux-surface reconstructions: Te(y)⇒ J and q

## Slide 13: Main radiation mechanisms: Bremsstrahlung (ff), radiative recombination (fb) & line-emission (bb)

## Slide 14: Coronal equilibrium (ionization charge balance)
Commonly used in fusion plasmas and in the solar corona
Assumes three body-recombination rate is small
Balance between electron-impact ionization & radiative recombination
Result: Ionization degree is independent of density and increases with Te
Low-Z ions (Be, B, C) are often fully stripped

## Slide 15: Fractional abundance calculations (nij/ni) depend only on the local electron temperature (issues with nomenclatures ???)
Fully
stripped
H-like
He-like
Fully
stripped
H-like
He-like
Argon
Z=18
A~40
18 protons
22 neutrons
Calcium
Z=20
A~40
20 protons
20 neutrons

## Slide 16: Local emission has to be calculated on plasma parameters [Te, ne, nZ(R,t)]
Continuum and & line emission:
Bremsstrahlung (ff):
Radiative recombination (fb):
Line emission (bb):
Continuum:
exp(-hn/kBTe)
Line-emission:
∝nAl
Continuum:
exp(-hn/kBTe)
∝nMo
∝nMo
0.1
10
Te [keV]

## Slide 17: Take home message: You have four basic alternatives to measure radiation from plasmas
Conventional radiated power measurements (integrate all) (e.g., radiated power density ⇒ power balance)
Conventional “broadband/filtered” x-ray measurements (e.g., SXR tomography ⇒ confinement, MHD, equilibrium)
Conventional vs modern broadband PHA & multi-energy measurements (e.g., Zeff, nZ, Te, ne,fast)
Doppler line-radiation x-ray measurements (e.g., nZ, Te, Ti, vf, vq, ⇒ calculation of Er)

## Slide 18: 1) Radiative power densities (vis/UV/x-ray) & charge state <Z> can be obtained using coronal equilibrium
Equations of interest for two-impurity plasma
Quasi-neutrality:
Effective charge:
Normalized radiated power density:
Hydrogenic cooling rate:
Radiated power in the purely hydrogenic case (Zeff=1)

## Slide 19: Class-Homework #3: NSTX-U…on the “fly”
1) For a core DD NSTX-U plasma of 1 keV and a typical ne,0 of 8.0×1019 m-3, calculate:
The deuterium concentration (nD/ne), plasma effective charge (Zeff) and radiated power density Prad [W/m3] assuming a carbon concentration of 2% (HINT: no other impurities)
How large is Prad if one compares to the purely “ideal” hydrogenic value?
Quasi-neutrality:
Effective charge:
Normalized radiated power density:

## Slide 20: Class-Homework #3: NSTX-U…on the “fly”
1) For a core DD NSTX-U plasma of 1 keV and a typical ne,0 of 8.0×1019 m-3, calculate:
The deuterium concentration (nD/ne), plasma effective charge (Zeff) and radiated power density Prad [W/m3] assuming a carbon concentration of 2% (HINT: no other impurities)
How large is Prad if one compares to the purely “ideal” hydrogenic value?
The nD/ne, Zeff and Prad if one includes also 0.5% of oxygen
Now, how large is the new Prad if one compares to the purely “ideal” hydrogenic value?
Now, add iron at nFe/ne~0.1%, and repeat calculations for nD/ne, Zeff and Prad
How large is the new Prad if one compares to the purely “ideal” hydrogenic value?
The change in neutron flux from the ideal case (nD=ne) when adding carbon, oxygen and iron cases (HINT: Sn=nDnDsDD(Ti) and use dilution results from a), c) and e))
EXTRA
EXTRA
EXTRA

## Slide 21: Class-Homework #4: ITER…for “home”
2) For a typical ITER DD plasma with an average electron density of 1.0×1020 m-3 and an average electron temperature of 8.8 keV (see http://fusionwiki.ciemat.es/wiki/ITER) calculate:
nD and Zeff assuming Be and W concentrations of 10% and 0.001%, respectively.
Increase the CW to a more realistic 10-4 and repeat the calculation in 2-a).
The change in neutron rate when changing the tungsten concentration from 10-5 to 10-4
Calculate the core radiated power density [W/m3] from all the ion constituents [e.g. H or D and Be for both cases of cW @ 10-5 and 10-4].
What fraction of the total input power is radiated away for the case of 10-1 of Be and 10-4 of W? Consider an average volume for ITER with an elliptical cross section of the order of VITER~pab×2pR0, where “a” is the minor radius (~2m), “R0” is the major radius of about 6 m and we consider an ellipticity (b/a) of about 1.5.
EXTRA

## Slide 22: Let's get real…why is this important?
Rotation-induced Dj, Er, nZ, Zeff and Prad asymmetries in NSTX

## Slide 23: Let's get real…what do we conclude?
Rotation-induced Dj, Er, nZ, Zeff and Prad asymmetries in NSTX
While the asymmetry in the core radiated power density from low-Z ions is relatively small, the 2D radiation profiles from medium- to high-Z’s are strongly affected by centrifugal forces.

## Slide 24: Radiation measurements are line-integrated along detection sightlines
Transport/heating asymmetries (warning):
Example:
Core radiation from medium- to high-Z will be affected by centrifugal forces
Visible/UV/x-ray radiated power tomography:
Emissivity is a flux-surface function
Inversion (B=M×E ⇒ E=M-1×B)

## Slide 25: Radiated power density measurements (no spectral resolution) use metal-foils or Si-diodes + electronics
Metal foil bolometers
Si diodes

## Slide 26: 2) Conventional tomography integrates in photon-energy using metal filters, diode arrays and TIAs
MIT
PSFC
AXUV-20
Direct x-ray detection
(e.g. Si diodes)
Conventional tomography integrate in energy-space
Example of spatially resolved x-ray spectra from ITER
Indirect detection
with scintillator
(e.g. CsITl - green)
AXUV-100
Typical EUV-UV Photon Response
SXR
1 cm2

## Slide 27: Conventional SXR tomography consists of an array of diodes/detectors integrating the local plasma emissivity
Essential elements:
Pinhole (radial resolution vs integration)
Thin vs thick metallic filters (e.g., Be)
Current mode: SXR Si-based diode or diode-array
Current mode: X-ray scintillator + FoP + FO + PMT
Transimpedance amplifier (104-107 V/A) + DAQ
Metal filters discriminate edge/core effects
(peeling the “onion”)
What happens if we don’t use a filter?
Filters: see CXRO website x-ray database
https://henke.lbl.gov/optical_constants/

## Slide 28: Conventional soft x-ray (SXR) tomography is still being used for stability, MHD & transport studies
MIT
PSFC
b) Impurity transport (e.g. using gas injection or LBO)
a) Stability and MHD [e.g. (m,n) modes and sawteeth]

## Slide 29: Take home message: You have four alternatives to measure radiation from plasmas
Conventional radiated power measurements (integrate all) (e.g., radiated power density ⇒ power balance)
Conventional “broadband/filtered” x-ray measurements (e.g., SXR tomography ⇒ confinement, MHD, equilibrium)
Conventional vs modern broadband PHA & multi-energy measurements (e.g., Zeff, nZ, Te, ne,fast)
Doppler line-radiation x-ray measurements (e.g., nZ, Te, Ti, vf, vq, ⇒ calculation of Er)

## Slide 30: How to extract plasma physics parameters from wide and narrow energy bands ?
4) Narrow energy bands
Doppler spectroscopy
High-resolution spectrometers
E/DE~5000-200000
Probes mainly the ion-channel
Ti, Vf,q, nZ… Te (line-ratios)
Narrow bands
Wider
band
Spatially resolved x-ray spectra from ITER
3) Wider energy bands
Multi-energy spectroscopy
Low-resolution spectrometers
E/DE~10-50
Probes e- and ion channels
Te, nZ, DZeff, Zeff
ne,fast (e.g. LHCD, runaways)

## Slide 31: Conventional photon counting ME-SXR systems use Si(Li), HgI2, Si-Ge-CdTe diodes and SDDs
Detectors in photon-counting mode
(<Te>, <Zeff>, <ne,fast>, <nZ>)
    Pulse height analysis (PHA)
    Good energy resolution (100-200 eV)
    Slow time-response (20-50 ms)
    Low efficiency at high-energies
    Very poor profile definition
    Still used in our community
    (HT7, TCV, HL-2A)
106 CPS
Amptek
Ketek
Single-chord spectrometers
One spectrum per instrument

## Slide 32: New PILATUS detectors enables breakthrough of 100k pixels (minimum) at single or multiple energy ranges
CMOS
readout chip
Si-sensor
2D array pn diodes
In
balls
PILATUS 100K
106 CPS/p
Operates in single photon counting mode
CMOS hybrid pixel technology developed originally for synchrotrons (CERN + PSI + DECTRIS)
Thanks to important advances in the x-ray detector technology it is now possible to simultaneously record high resolution images of x-ray photons at single OR multiple energy ranges through direct x-ray detection.
100K to 12M pixels
(PILATUS: 172 mm,
EIGER: 75 mm)
PILATUS3 900K-IPP in-vacuum detector for x-ray plasma spectroscopy
(dimensions of a 100K system: 487x195 pixels)

## Slide 33: Initial ME-SXR imaging tests in C-Mod (@MIT) combined the best features from PHA & multi-foil methods
From sampling the continuum radiation from Ar & Mo one can measure Te & ne2Zeff
Pin-hole camera with multi-energy pixels allowed simultaneous spatial and energy resolution

## Slide 34: Comparator and triming voltages on each pixel allow individual coarse & fine tuning of energy range
EW~500 eV
“Constant” width of electronic response is a great improvement over the use of filters
Filters: CXRO website:
X-ray database
PILATUS technology:
photon counting circuit in each pixel

## Slide 35: How to extract plasma physics parameters from wide and narrow energy bands ?
4) Narrow energy bands
Doppler spectroscopy
High-resolution spectrometers
E/DE~5000-200000
Probes mainly the ion-channel
Ti, Vf,q, nZ… Te (line-ratios)
Narrow bands
Wider
band
Spatially resolved x-ray spectra from ITER
3) Wider energy bands
Multi-energy spectroscopy
Low-resolution spectrometers
E/DE~10-50
Probes e- and ion channels
Te, nZ, DZeff, Zeff
ne,fast (e.g. LHCD, runaways)

## Slide 36: X-ray crystal imaging spectrometers revolutionized our field with Ti and Vf,q profile measurements
Similar systems have been installed in NSTX, KSTAR, EAST, LHD, W7 and in the future, NSTX-U, WEST, JT60SA & ITER

## Slide 37: Crystals help achieving high-spectral response (E/DE>104) for high-resolution Te,i & vf,q measurements
Bragg diffraction:
Assuming a constant “d”, the observed relative wavelength shift (DS: Doppler shift) is given by:
The value of Dqmax from Johann error (Je):
Resolving power:
v is the relative velocity between the source & detector

## Slide 38: Focusing properties of spherical x-ray crystal
Rowland circle
(r=Rc/2)
Magnetic axis
fm
fs
Typical distances from the crystal:
Meridional focus:
Sagittal focus:

## Slide 39: Electron temperature Te-profiles can also be obtained using line-ratios between resonance and satellite lines
(L. Delgado-Aparicio, un-published)
He-like Ar
spectra
Te-measurements based on the ratio of the resonance line-w and the dielectronic satellites “n=3” and “k”
Considered to be a secondary diagnostic technique for the electron temperature (Te) JT60SA and ITER.

## Slide 40: Summary: Modern radiated power diagnostics can help study and resolve Prad, nZ, Te,i, Vf,q, Zeff & ne,fast profiles
With the selection of W for the divertor in ITER, understanding the sources, transport and confinement of high-Z impurities is crucial to ITER success.
A significant fraction of the power delivered to the plasma is lost in the form of radiation. In the x-ray range (subset of Prad) could be as high as 90%.
Modern diagnostics for overall radiated power and “filtered” spectroscopy allow us to probe Prad, nZ, Te,i, Vf,q, Zeff & ne,fast and their profiles!

## Slide 41: Join us: New core diagnostics (US-lead) will be installed in NSTX-U, MST, WEST, W7X, JT60SA and ITER
ITER
DEMO ?
WEST - France
JT60SA

## Slide 42: Don’t forget about the non-axisymmetric systems and alternative concepts
Stellarators (Ip~0)
LHD
@NIFS
in Japan
W7X
@MPIPP
in Germany
CMFX @ UMD & UMBC
WHAM @ UW-Madison
Magnetic mirrors

## Slide 43: …And opportunities also in the private sector!
Notable investments in 2021-22
Extraordinary opportunities for public-private-partnerships (PPPs)
GF
Zap
TAE
CFS
TE