## Slide 1: Introduction to Low Temperature Plasmas
Amanda M. Lietz
Department of Nuclear Engineering, North Carolina State University
2024 Introduction to Plasma and Fusion Course
June 17, 2024

## Slide 2: Dr. Lietz’s Technical Background
Assistant Professor in NCSU Nuclear Engineering Department since August 2022.
B.S., Nuclear Plasma and Radiological Engineering from University of Illinois at Urbana-Champaign
PhD, Nuclear Engineering and Radiological Sciences at University of Michigan
  Atmospheric Pressure Plasma Sources for Plasma Medicine
  Primarily fluid and global modeling
  Laser diagnostics
Postdoctoral Appointee at Sandia National Laboratories
  Thermionic energy converters, mass spectrometers, validation, semiconductor processing
  Primarily particle-in-cell simulations
2

## Slide 3: Dr. Lietz’s Personal Background
Participated in this course in 2012!
Notes: Illinois hired first female faculty, pregnant on every job interview, kids

## Slide 4: Computational Plasma Science (ComPS) Group
Modeling Low Temperature Plasmas.
Established in August 2022.
Tackling these problems involves using existing tools and developing new tools.
G. Xu, X. Shi, J. Cai, S. Chen and P. Li, Wound Repair Regen. 23, 878 (2015).
“Plasma Process Metrology” www.nist.gov
Application Areas of Interest:
  Semiconductor Processing
  Fusion Technologies
  Biomedical Applications
  Chemical Conversion
  Laser-produced Plasmas

## Slide 5: Agenda
Defining a Low Temperature Plasma (LTP)
Conceptual Derivation of a Sheath
Non-equilibrium and non-Maxwellian in LTPs
Applications of LTPs
The Role of Computational Modeling
Learning objectives:
  Explain why Te >> Tgas.
  Name several applications of LTPs.
  Describe a sheath.

## Slide 6: What is a Low-Temperature Plasma?
Solvay
-
+
e-
e-
e-
+
e-
e-
+
e-
e-
+
E
Low temperature plasma – plasmas with a gas temperature much less than what would cause ionization.
Electrons are heated by an electric field.
  Te >> Tgas
Sustained by electron-impact ionization.
  e + M → M+ + e + e
Angstrom engineering
Notes: Explain fluorescent light bulbs

## Slide 7
“Plasma Science: Advancing Knowledge in the National Interest” National Research Council of the National Academies Report (2007).
…

## Slide 8
In order to have a plasma, some energy needs to be high enough to cause an ionization.
In a thermal plasma (i.e. the sun) : Tgas ~ Eiz (10 eV, 110,000 K)
Low-temperature plasmas use E-fields, which selectively accelerate electrons.
  m = mass,
  v = velocity,
  e = elementary charge,
  E = constant electric field
Ignoring collisions.
Low temperature plasmas also tend to be weakly ionized – only a ppb/ppm is charged species.
Low-Temperature Plasmas

Electrons
Ions

## Slide 9: Plasma Chemistry: Electron Impact Reactions
Elastic Collision (all energies)
  e + He  He + e
  Billiard balls, electron loses energy to gas heating
Ionization (4 – 25 eV)
  e + He  He+ + e + e
Electronic excitation (1-10 eV)
  e + He  He* + e
  Can emit a photon
Vibrational excitation (0.1-1 eV)
  e + N2(v=0)  e + N2 (v0)
Dissociation (1-15 eV)
  e + N2  N + N + e
Dissociative ionization (10-20 eV)
    e + N2  N + N+ + e + e
Attachment (low energy)
  e + O2 + M  O2- + M
Dissociative attachment (low energy)
  e + O2  O- + O
Superelastic collision (low energy)
    e + He*  He + e
Energetic electrons collide with neutral atoms/molecules.
e-
e-
N
N
N
N

## Slide 10: SHEATHS

## Slide 11: Start with an “ideal” plasma
11
Let’s initialize a perfectly uniform plasma
In a gap between two infinite surfaces.
ne = electron number density
ni = ion number density
Number Density
Potential
V
Position
ne = ni

## Slide 12: Fluxes to Surfaces
12
Flux – the number of particles passing through a surface, per unit area, per unit time.
The thermal flux in a gas is
n = number density
vth = average thermal speed
Even if ,
Number Density
ne = ni
e
e
i
i
Lose e- faster because they’re moving faster!
Potential
V
Position

## Slide 13: Plasma Potential Develops
13
An instant later…
You only need to lose a very small fraction of the electrons to create a significant electric potential.
This electric field near the walls changes the fluxes.
Number Density
ne < ni
Position
e
e
i
i
Potential
V
ne = ni
ne < ni

## Slide 14: Steady State – Sheath!
14
The self-generated electric field stops growing when the fluxes balance.
When a charged particle approaches the wall, this potential
  Decelerates electrons
  Accelerates ions
Plasma tends to be the most positive thing in the system.
  If you apply a positive voltage, the plasma potential will increase above that.
Number Density
ne < ni
Position
e
e
i
i
Potential
V
ne = ni
ne < ni

## Slide 15: Now we have a sheath!
15
Sheath is a few D thick
Sheaths form at all wall surfaces in contact with the plasma
The plasma is the most positive thing in the system (“Plasma potential”)
The potential profile accelerates ions and repels electrons.
Because electrons are hot, many of them have enough energy to overcome the potential gradient.
-
-
-
-
-
-
-
-

## Slide 16: ELECTRON ENERGY DISTRIBUTIONS

## Slide 17: Plasma Chemistry: Electron Impact Reactions
Elastic Collision (all energies)
  e + He  He + e
  Billiard balls, electron loses energy to gas heating
Ionization (4 – 25 eV)
  e + He  He+ + e + e
Electronic excitation (1-10 eV)
  e + He  He* + e
  Can emit a photon
Vibrational excitation (0.1-1 eV)
  e + N2(v=0)  e + N2 (v0)
Dissociation (1-15 eV)
  e + N2  N + N + e
Dissociative ionization (10-20 eV)
    e + N2  N + N+ + e + e
Attachment (low energy)
  e + O2 + M  O2- + M
Dissociative attachment (low energy)
  e + O2  O- + O
Superelastic collision (low energy)
    e + He*  He + e
Energetic electrons collide with neutral atoms/molecules.
e-
e-
N
N
N
N

## Slide 18
Electron Energy Distribution Functions (EEDFs)
Cheng Ling Kuo, Advances in Spacecraft Systems and Orbit Determination.
Must use cross sections (instead of rates) for electron impact reactions.

## Slide 19
Energy distributions can be significantly non-Maxwellian.
A Maxwellian distribution is linear in these units.
Hagelaar, Pitchford. Plasma Sources Sci. Technol. 14, 722 (2005).
Electron Energy Distribution Functions (EEDFs)
Solve Boltzmann’s equation in 0D using a spherical harmonic expansion of the EEDF:
This is used to calculate reaction rates, k(Te).
Sometimes fully kinetic (Monte Carlo) methods are required.
Cheng Ling Kuo, Advances in Spacecraft Systems and Orbit Determination.
Must use cross sections (instead of rates) for electron impact reactions.
Maxwellian

## Slide 20: Maxwellian Distribution Function, f(v)
2.5 eV
Units : s3/m3
Same distribution, plotted in 3V space
Spherical symmetry

## Slide 21: Anisotropic Distribution Functions
Add an electric field and neutral collisions
  Multibolt simulations, 2-term
  He, Biagi database, E/N = 100 Td
B = 0
Ez
Same distribution, plotted in 3V space
Symmetric about E-field axis
Notes: Can you tell the direction of the drift?

## Slide 22: What’s the Temperature of this?
Some say it doesn’t have one.
Convention in the field:
For Maxwellian, this converges to the standard definition of temperature.
Ez
Notes: Can you tell the direction of the drift?

## Slide 23: Reduced Electric Field
E/N is an important parameter in low temperature plasmas.
E = electric field
N = gas number density
Electron energy equation
Power
Elastic collisions
Inelastic collisions
Notes: Can you tell the direction of the drift?

## Slide 24: Reduced Electric Field
E/N is an important parameter in low temperature plasmas.
E = electric field
N = gas number density
The electron energy is a function of E/N (independent of ne).
  Based on the assumption that electron neutral-collisions are the main electron energy loss.
We solve Boltzmann’s equation for electrons for a particular E/N in a given gas mixture.
1 Td = 10-17 Vcm2
Electron energy equation
Steady state, approximate conductivity
Notes: Can you tell the direction of the drift?

## Slide 25: NON-EQUILIBRIUM THERMODYNAMICS

## Slide 26: Fighting Thermodynamics
In most LTPs,
Te >> Ti ~ Tgas
How do we maintain this high Te?
We keep heating the electrons.
This is much easier in atomic gases (He, Ar) than molecular gases.
Vibrational/rotation excitation has a low threshold energy, the second term is very large.
Electron energy equation
Decreasing Te

## Slide 27: Fighting Thermodynamics
Vibrational/rotation excitation has a low threshold energy, the second term is very large.
Vibrational-translational energy transfer rapidly converts electron energy into gas heating
N2(v) + M  N2 + M
Short pulses (nanoseconds) can keep Tgas >> Te
Limits total energy deposition so natural heat transfer can keep Tgas low.
The plasma never reaches a steady state.
Electron energy equation

## Slide 28: Dielectric Barrier Discharges (DBDs)
At atmospheric pressure, high collisionality results in short timescales and rapid evolution.
Need to limit the energy deposition, prevent arc formation and gas heating.
Dielectric barrier discharges (DBDs) – a pulsed discharge in which at least one electrode is covered by a dielectric.
Discharges last ~10-8 s, repeat every ~10-3 s.
K. G. Kostov, et al., Brazilian J. of Phys. 39, 322 (2009).
Y. Hosokawa et al., J. Phys. D: Appl. Phys., 41, 205418 (2008).
J.-C. Wang, PhD Thesis, (Univ. of Michigan, 2014).

## Slide 29: LTP APPLICATIONS

## Slide 30: Plasma Medicine
Atmospheric pressure plasma treatment
  Improves wound healing
  Selectively kills cancer cells
  Kill bacteria
  Heal dermatological lesions
Reactive oxygen and nitrogen species are thought to be responsible: OH, O, HO2, NO, etc.
Low temperatures are required.
Dielectric barrier discharges (DBD) and atmospheric pressure plasma jets (APPJs) are popular types of sources.
Tissue is generally covered in a thin liquid layer of biological liquid.
G. Fridman et al., Plasma Chem. Plasma Process. 26, 425 (2006).
K. D. Weltmann et al., J. Phys. D: Appl. Phys. 41, 194008 (2008).
G. Xu, X. Shi, J. Cai, S. Chen and P. Li, Wound Repair Regen. 23, 878 (2015).

## Slide 31: Wound Healing
An example of a typical plasma medicine study.
Two wounds were generated on each mouse, and one was plasma treated.
S = area of plasma treated – area of control (averaged over all mice)
Optimal healing with 30 s of plasma treatment each day.
Currently these effects cannot be attributed to a single reactive species.
G. Xu, X. Shi, J. Cai, S. Chen and P. Li, Wound Repair Regen. 23, 878 (2015).
  Day 1 Day 4 Day 7
  Plasma Treated
  Control
  Control
  Plasma Treated

## Slide 32: Water Treatment
Plasmas have been used to create O3 for water treatment since the 1800s.
Direct treatment of water with plasma is an emerging application.
Targeting removal of PFAS ‘forever chemicals’.
For must be extremely scalable, rapid, and inexpensive (usually in air).
J. E. Foster, Phys. Plasmas 24, 055501 (2017)
O. Galmiz, et al., J. Phys. D. Appl. Phys. 49, 65201 (2016).
water
water

## Slide 33: Semiconductor Processing
When a plasma contacts a surface, a sheath develops:
  Electrons diffuse faster than ions.
  Plasma potential becomes positive.
  E-field develops which retains e-, accelerates ions.
This results in ions reaching the surface with significant energy (a few eV to keV).
Anisotropy occurs.
Reactive neutrals (e.g. Cl, F) formed from plasma chemistry work synergistically with ions for rapid etching.
Plasmas are also used to deposit thin films.
Without plasmas, computer chips would be stuck in the late 1980s or early 1990s.
Features are approaching atomic scales: atomic layer etching (ALE) and atomic layer deposition (ALD).
A. Galata, Physics and Technology of the SPES Charge Breeder (2005).
https://www.anandtech.com/show/17448/intel-4-process-node-in-detail-2x-density-scaling-20-improved-performance
30 nm features

## Slide 34: Plasma for the Grand Challenges
Make Solar Energy Economical
Thin film deposition for photovoltaics.
Nanostructures.
Use solar power to produce chemical fuels.
National Academy of Engineering
http://www.engineeringchallenges.org/challenges.aspx
Engineer Better Medicines
Killing drug-resistant pathogens.
Cancer treatments.
Wound healing.
Nanoparticle production.
Provide Access to Clean Water
Destruction of PFAS.
Ozone generation.
Provide Energy From Fusion
Temperatures of 105 eV.
Low temperature plasmas occur near the walls in magnetic confinement fusion.

## Slide 35: Plasma for the Grand Challenges
Manage the Nitrogen Cycle
Plasma nitrogen fixation to produce ammonia.
Direct production of nitrate.
Develop Carbon Sequestration Methods
Plasma dissociation of CO2 into CO.
Conversion of CO2 into useful chemicals.
Engineer the Tools of Scientific Discovery
Mass spectrometers.
Plasma thrusters for space exploration.
Quantum computing.
Chips Impact EVERY Challenge
Advance Personalized Learning
Enhance Virtual Reality
Reverse Engineer the Brain
Advance Health Informatics
Restore and Improve Urban Infrastructure
Secure Cyberspace
Prevent Nuclear Terror

## Slide 36: COMPUTATIONAL MODELING

## Slide 37: What can we really learn from modeling?
Helium atmospheric pressure plasma jet.
Cylindrical symmetry.
He flows into air.
Localized heating at the cathode expand launching an acoustic wave.
Perturbs shear flow.
We can turn off gas heating!
  Without changing dissociation, buoyancy, ion wind.
Animation Slide

## Slide 38: What can we really learn from modeling?
He atmospheric pressure plasma jet
Surrounding gas flow (shield gas) observed to influence plasma dynamics from optical emission measurements.
But why?
Comparison with a fluid model.
A. Schmidt-Bleker, et al., Plasma Sources Sci. Technol., 24, 035022 (2015).
Notes: What is electronegative N2

## Slide 39: References
“Principles of Plasma Discharges and Materials Processing” M. A. Lieberman and A. J. Lichtenerg

## Slide 40: Quick Review
E/N (Reduced Electric field) is the scaling parameter for LTPs.
  Acceleration between collisions.
Te >> Ti ~ Tgas
  Electrons are lighter, more energy is transferred to electrons than ions.
  We must deposit power to achieve this.
Sheaths form at surfaces, trapping electrons in the plasma, accelerating ions toward surfaces.
  These fast ions can be used for etching.
“Principles of Plasma Discharges and Materials Processing” M. A. Lieberman and A. J. Lichtenerg
-
-
-
-
-
-
-
-