## Slide 1: Integrated modelling for fusion devices
Presented by: Yashika Ghai
Position: R&D Associate staff- Theory and computation plasma physicist
Email: ghaiy@ornl.gov

## Slide 2: My background
2013 2014- 2019 2019-2021 May 2021- present
Ph.D. - Theoretical Plasma Physics –Space & astrophysical, Dusty plasmas
* Attended Lindau Nobel Laureates meeting 2016
ORNL post doc-
Started working on energetic particle physics in fusion plasmas
ORNL staff position- Theory and Computation Plasma physicist
Master’s- Summer internship at Institute of Plasma Physics (IPR), India

## Slide 3: Key Takeaways
Different theoretical and numerical models are used to describe the distinct plasma properties in the core and edge regions.
Integrated modelling is needed to perform comprehensive simulations of various physical processes and interactions within a fusion reactor
Combination of multiple models to optimize performance and predict behavior of a future reactor-relevant fusion device.

## Slide 4: Theoretical descriptions of Plasma
Plasma Models
Fluid Model
Magneto-hydrodynamics
Continuity Equation
Momentum Equation
Maxwell’s Equations (magnetized plasma)
Hybrid-models
Kinetic Model
Vlasov equation Maxwell’s Equations

## Slide 5: Theoretical descriptions of Plasma
Plasma Models
Fluid Model
Magneto-hydrodynamics
Continuity Equation
Momentum Equation
Maxwell’s Equations (magnetized plasma)
Hybrid-models
Kinetic Model
Vlasov equation Maxwell’s Equations

## Slide 6: Kinetic description
is the charged particle distribution function in 6-D position momentum space
Description of plasma in 2-D phase-space
Maxwell’s equations
Kinetic Vlasov-equation
Boltzmann equation
Assumption: on average, behavior of each particle is the same and independent of other particles, following only the prescriptions of the self-consistent field – collisionless plasma
Notes: assumption that on average behavior of each particle is the same and independent of other particles, following only the prescriptions of the self-consistent field

## Slide 7: Gyrokinetic equation in fusion plasmas
Due to strong magnetic fields in fusion plasmas, we take average of the Vlasov equation over the fast gyromotion, which leads to gyrokinetic equation
Perturbed distribution function
Gyro-averaged Maxwell’s equation (Electromagnetic waves)
Gauss’s law (Electrostatic waves)
+
Guiding center
Full orbit
Notes: The second term represents particle streaming along the magnetic field line. The third term contains the effects of cross-field particle drifts, including the curvature drift, the grad-B drift, and the lowest order E-cross-B drift. The fourth term represents the nonlinear effect of the perturbed E→×B→ drift interacting with the distribution function perturbation. The fifth term uses a collision operator to include the effects of collisions between particles. The sixth term represents the Maxwell–Boltzmann response to the perturbed electric potential. The last term includes temperature and density gradients of the background distribution function, which drive the perturbation. These gradients are only significant in the direction across flux surfaces, parameterized by ψ, the magnetic flux.

## Slide 8: Theoretical descriptions of Plasma
Plasma Models
Fluid Model
Magneto-hydrodynamics
Continuity Equation
Momentum Equation
Maxwell’s Equations (magnetized plasma)
Hybrid-models
Kinetic Model
Vlasov equation Maxwell’s Equations

## Slide 9: When we take moments of kinetic-Vlasov equation, we obtain fluid equations for plasma
Zeroth order moment : fluid density “n”
First order moment : Fluid velocity “u”
):
Maxwell’s equation (Electromagnetic waves)
Gauss’s law
(Electrostatic waves)
+
Average behavior of each species is sufficient to describe plasma dynamics- collisional plasmas

## Slide 10
Zeroth order:
First order :
Closure coefficient
Moments of gyrokinetic equation lead to gyrofluid equations for strongly magnetized plasma
Notes: Mention Hammett and Perkins closures

## Slide 11: Theoretical descriptions of Plasma
Plasma Models
Fluid Model
Magneto-hydrodynamics
Continuity Equation
Momentum Equation
Maxwell’s Equations (magnetized plasma)
Hybrid-models
Kinetic Model
Vlasov equation Maxwell’s Equations

## Slide 12: Fluid model in a magnetized plasma can be simplified to MHD model
2-Fluid model
Single fluid Magnetohydrodynamic model
Where,

## Slide 13: Theoretical descriptions of Plasma
Plasma Models
Fluid Model
Magneto-hydrodynamics
Continuity Equation
Momentum Equation
Maxwell’s Equations (magnetized plasma)
Hybrid-models
Kinetic Model
Vlasov equation Maxwell’s Equations

## Slide 14: Plasma modelling is to solve the differential equations and identify the spatiotemporal behavior of a plasma system
Depending upon the physics we want to resolve, we simplify our models by making assumptions
Discretize equations and use numerical techniques such as finite difference, finite elements for fluid equations
Runge-Kutta integrators for particle orbit following codes
PIC approach for solving kinetic equations
Finite difference, finite element/volume scheme for solving fluid equations

## Slide 15: Core and edge plasma conditions are very different in a fusion device
Property | Fusion Plasma Core | Fusion Plasma edge
Temperature | Extremely high, ~keV | Much cooler compared to the core (1-100 eV)
Density | Higher particle density | Lower particle density
Magnetic fields | Stronger and more uniform | Weaker and more turbulent
Particle behavior | Highly energized and relatively stable | More turbulent and irregular
Confinement | Better confinement properties | Poorer confinement due to increased turbulence
Impurities | Relatively cleaner with fewer impurities | More impurities from interactions with reactor walls

## Slide 16: Dynamics of core plasmas are defined by gyrokinetic models whereas edge plasmas are defined by fluid models

## Slide 17: Integrated Modelling for fusion reactor design

## Slide 18: What is integrated modeling?
Coupled models of fusion plasma physics and engineering in an integrated workflow to perform self-consistent multi-physics, multi-fidelity, iterative calculations for a fusion reactor design

## Slide 19
FREDA (Fusion Reactor Design and Assessment)-SciDAC is a purpose-built framework for multi-fidelity, iterative optimization- led by Cami Collins, ORNL
FREDA aims to catch and solve ‘show-stoppers’ at the appropriate fidelity level using self-consistent assessment & design optimization
Will initially apply to tokamaks/STs, potential for expansion to stellarators
Notes: FREDA consists of 3 main components, plasma, geometry generation, and engineering analysis

## Slide 20: Approach: flexible component-based framework & data structure
Edge
Plasma State File
Driver
Engineering State File
Driver
Driver
System State File
Core
FASTRAN
TGLF
NCLASS
EFIT
DCON
GATO
NUBEAM
TORAY
GENRAY
Neutronics/ Tritium
MCNP
SHIFT
Structural Mechanics
DIABLO
Thermal Hydraulics
openFOAM
EM
Elmer
openFOAM
CFD
openFOAM
EPED
SOL
C1
SOLPS
Geometry State File
TF coil
PF coil
Divertor
First Wall
Blanket
CS coil
Driver
Includes Multiphysics simulation tools
Based on the open-source IPS (Integrated Plasma Simulator)
Includes systems codes and parameterized geometry representation
Fusion-Plasma
Fusion-Engineering
Parametric Geometry
Capable of integrating swappable modules with diverse CPU/GPU requirements
Framework & Workflow
C2
Notes: Feedback to statefile and run core transport codes to analyze how redistribution affects thermal profiles.

## Slide 21: Approach: flexible component-based framework & data structure
Edge
Plasma State File
Driver
Engineering State File
Driver
Driver
System State File
Core
FASTRAN
TGLF
NCLASS
EFIT
DCON
GATO
NUBEAM
TORAY
GENRAY
Neutronics/ Tritium
MCNP
SHIFT
Structural Mechanics
DIABLO
Thermal Hydraulics
openFOAM
EM
Elmer
openFOAM
CFD
openFOAM
EPED
SOL
C1
SOLPS
Geometry State File
TF coil
PF coil
Divertor
First Wall
Blanket
CS coil
Driver
Includes multiphysics simulation tools based on Fusion Energy Reactor Models Integrator (FERMI)
Based on the open-source IPS (Integrated Plasma Simulator) developed in AToM SciDAC
Includes systems codes and parameterized geometry representation
Fusion-Plasma
Fusion-Engineering
Parametric Geometry
Capable of integrating swappable modules with diverse CPU/GPU requirements
Framework & Workflow
C2
Where is energetic particle physics needed in an integrated framework?
Notes: Feedback to statefile and run core transport codes to analyze how redistribution affects thermal profiles.

## Slide 22: Energetic particles have higher temperature in comparison to thermal plasma
Energetic particle sources:
Injecting high energy neutral particles (NBI) to heat plasma (NBI).
energetic alpha particles as by-product of fusion reactions.
High energy Runaway electrons produced during thermal quench in disruptions or Tritium beta decay
3.5MeV
14 MeV
Alfvén instabilities
Whistler instabilities
ITER- International Thermonuclear Experimental Reactor
https://www.atomicarchive.com/science/fusion/index.html,

## Slide 23
Perturbation
Alfvén eigenmodes in ITER
, where ,
Alfvén Wave dispersion relation :
is the Alfven speed.
Alfvén waves are transverse electromagnetic waves created by perturbations in the magnetic field lines.
Alfvén eigenmodes is a special class of Alfvén wave that exist in fusion devices due to periodic boundary conditions imposed by the machine’s geometry.

## Slide 24: Challenge- Waves may interact resonantly with charged particles and can become unstable
FM radio is tuned to resonate with certain frequencies that correspond to a particular radio station/channel
In plasmas, surfer riding a wave picture demonstrates Landau resonance phenomena between charged particles and plasma waves
Source: https://en.wikipedia.org/wiki/Landau_damping

## Slide 25: How do energetic particles cause Alfvén instabilities?
[Pace, Physics Today (Oct. 2015)]
[Pace, Physics Today (Oct. 2015)]
Energy exchange can occur via Landau resonance as the ion stays in phase with the wave as it traverses the mode.
Gradients in real space drive instability,
Can cause redistribution that affects core performance or loss of fast ions that damage the first wall materials.
Bump-on tail distribution cause inverse Landau damping
Source: https://commons.wikimedia.org/wiki/File:Bump_on_tail_dist.png
Notes: Not just gradients in velocity space rather gradients in real space drive the instability, E.J power transfer

## Slide 26: To demonstrate an economically viable fusion energy source energetic alpha particle confinement is necessary
 | Fusion Gain | a-Heating Fraction | Scientific Frontier
Scientific Breakeven | Q = 1 | 17% | Alpha confinement
Burning Plasma Regime | Q = 5 | 50% | Alpha heating; Alpha effects on energetic particle instabilities
 | Q = 10 | 67% | Strong alpha heating; Non-linear coupling effects
 | Q = 20 | 80% | Burn Control; potentially strong non-linear coupling
 | Q = ∞ | 100% | Ignition

## Slide 27: Theoretical Model for FAR3d code
Thermal Plasma
Reduced MHD equations-
Ohm’s law &
Vorticity
Compressibility effects-
Continuity & momentum equation
Energetic Particles
Gyrofluid Model with precise emulations of kinetic effects
Computationally efficient by truncating moments of gyrokinetic equation with appropriate closures for kinetic effects

## Slide 28: FAR3d pseudo-spectral representation
Dynamical (time-evolving) variables:
Equilibrium (steady-state) quantities:
Axisymmetric tokamak
Stellarator with field period symmetry (Nfp field periods)
Uses finite-differences in the radial direction and Fourier expansions in two angular variables to evolve the dynamic physical variables until convergence is met.

## Slide 29: Structure of FAR3d equations:
Solution vector evolution equations,
N is the nonlinear term
Semi-implicit approximation for N = 0
Semi-implicit solution for N = 0
Degrees of freedom (size of L, R, y): (number of equations) x radial grid points x number of Fourier modes x 2 Can be 105 to 106 for linear runs, 5 to 10 times larger for nonlinear runs.

## Slide 30: Linear Solver
The linear system is solved at each time step.
This is done as a two-step process using the direct block tridiagonal solvers CDECBT and CSOLBT developed by Alan Hindmarsh.
L and R have bloc-tridiagonal structure:
mj block rows = # of radial grid points
A, B, C are square sub-matrices with dimensions of NxN where N = 2 x # Fourier modes x number of equations
Numerical schemes used: i) a semi-implicit initial value solver which calculates the dominant mode (having the largest growth rate) ii) an eigenvalue solver calculates the stable and unstable (sub-dominant modes).

## Slide 31: Alfven eigenmodes observed in DIII-D
Input profiles:

## Slide 32: Reversed Shear Alfven Eigenmode (RSAE)
Electrostatic potential eigenfunction plot for n=1 at fast particle beta=0.0042, vth,f/vA=0.14, showing an m=4 RSAE mode with frequency 35 KHz and growth rate=0.011 .
1-D eigenmode plot
poloidal cros-section plot
2-D eigenmode structure in DIIID tokamak.

## Slide 33: Reversed Shear Alfven Eigenmode (RSAE)
Electrostatic potential eigenfunction plot for n=1 at fast particle beta=0.0042, vth,f/vA=0.14, showing an m=4 RSAE mode with frequency 35 KHz and growth rate=0.011 .
poloidal cros-section plot 3-D eigenmode structure in DIIID tokamak.

## Slide 34: Challenge: Energetic alpha particle transport and losses may limit performance of a reactor-level fusion device
How to study role of alpha particle transport on performance of a reactor-level fusion device?
Existing simulation codes take weeks on supercomputers to perform calculations of EP transport
Impractical to run in integrated scenarios for FPP design calculations
Present experiments
Future fusion
devices

## Slide 35: Goal: Develop a surrogate model of alpha transport using nonlinear FAR3d simulations
Output (EP transport flux)
Input (EP density gradient)
FAR3d simulations of ITER steady state case
  Highly nonlinear transport depends on multiple profiles and parameters
  Need to use techniques such as deep neural networks, transfer learning, etc.
Faster and accurate predictions of EP transport will be included in integrated framework for several applications, viz.
  Fusion pilot plant design and optimization
  Real-time prediction of burn control

## Slide 36: Key Takeaways
Different theoretical approaches to describe plasma
  Fluid, kinetic, MHD, hybrid
Resonant interactions between energetic particles and plasma waves driven plasma instabilities
Plasma instabilities can in-turn transport and de-confine energetic particles-can be harmful or useful
To design a future fusion reactor, we need to couple the physics of different regions of plasma in a single integrated framework- including the alpha particle physics via developing machine learning based surrogates.

## Slide 37: Picture with Prof. Takaki Kajita during Lindau meeting

## Slide 38: Toroidal coordinates

## Slide 39: Effect of fast particle
With increase in fast particle beta, no change in the type of eigenmode is observed.
However, an increase in growth rate is clearly indicated which due to increase in fast particle pressure and hence increased transfer of energy to Alfven eigenmode.

## Slide 40: Effect of fast particle energy via vth,f/vA
With increase in energy of neutral beam, transition takes place from RSAE to EAE mode.
An increase in growth rate is observed with increase in beam power and a peak in growth rate is observed for n=4 for which
A factor governing energy exchange is the alignment of energetic particle orbit with the eigenmode. Extracted energy scales linearly as long as the particle orbit is small compared to radial extent of the mode and Radial extent shrinks with n-1 .